## Slide 1
The Data Fusion automatic processing pipeline at CTBTO
Joshua Kunkle, Noriyuki Kushida, Martin Kalinowski , Robin Schoemaker, Jolanta Kuśmierczyk-Michulec, Boxue Liu, Yuichi Kijima
CTBTO
Presentation Date: 22 June 2023
PTS-520

## Slide 2
The International Monitoring System
PTS-520
The CTBTO monitors the earth for possible nuclear explosions through the International Monitoring System (IMS) which is composed of,
Data Fusion aims to provide the most comprehensive view of any event by matching information from Seismic, Hydroacoustic, Infrasound events to measurements at Radionuclide stations

## Slide 3
Data Processing at the International Data Center
PTS-520
Seismic
Hydroacoustic
Infrasound
Radionuclide
LEB
SEL1/
SEL2/
SEL3
REB / SEB
SSEB
Station Data
Station Processing
Analyst Review
Global Association
Atmospheric Transport Modeling
ARR
RRR
Products

## Slide 4
Data Fusion Pipeline at the International Data Center
PTS-520
Seismic
Hydroacoustic
Infrasound
Radionuclide
LEB
RRR
SEL1/
SEL2/
SEL3
ARR
REB / SEB
SSEB
Station Data
Automatic
Station Processing
Analyst Review
Global Association
Atmospheric Transport Modeling
Data Fusion Pipeline
Fused Events
Products

## Slide 5
IDC processing Outputs
PTS-520
Waveform
Radionuclide
Data from multiple measuring stations are combined to produce the most likely event time and location with an error ellipse
Nuclide concentrations are extracted from gamma-ray energy spectra
Nuclides Quantified | Half-Life | Conc (uBq/m3) | RelErr (%) | Activ (uBq) | RelErr (%)
BE-7 | 53.290 D | 5.1eE+03 | 2.32 | 6.27E+07 | 2.32
PB-212F | 10.64 H | 4.01E+04 | 1.98 | 5.65E+07 | 1.98
Data fusion aims to join these two types of results to produce combined hypotheses

## Slide 6
Atmospheric Transport Modeling
PTS-520
Atmospheric Transport Modeling (ATM) provides a connection between waveform-based events and radionuclide monitoring stations
T – 10h
T – 115h
SRS (m-3)
webgrape.ctbto.org
ATM Simulates the propagation of passive tracers through the atmosphere based on wind-field data
It is computationally expensive to perform the forward-in-time simulation for each waveform event
Instead, we perform backward-in-time simulation from each detecting station.
  Produces Source Receptor Sensitivity (SRS) Field
  Traces backward in time for 14 days
  Current resolution is 1 hour, 0.5 x 0.5 deg

## Slide 7
Data Fusion Methodology
PTS-520
Longitude
Latitude
T – 10h
T – 115h
SRS (m-3)
webgrape.ctbto.org
Follow ATM simulation backwards from each RN station
Overlap is accomplished by considering all grid elements which match an SHI ellipse at the event time
Waveform events
RN samples
Results in many-to-many relationship between RN samples and waveform events.
This is the maximal set of possible matches, which must be further processed

## Slide 8
Data Fusion Methodology
PTS-520
Visualize fusion with time – latitude projection
T – 10h
T – 115h
…
…
Backward simulation start at station location
14-day duration

## Slide 9
Delayed Releases
PTS-520
Achieved by releasing the requirement on the time component of the overlap
Results in a series of matched SRS values
SRS time series can be further used to quantify match probability
Prediction from full SRS field
Prompt
[1] A. Ringborn et al., “Radioxenon detections at CTBT international monitoring system likely related to the announced nuclear test in North Korea on February 12, 2013”, Journal of Environmental Radioactivity 128 (2014) 47-63
60 day limit is motivated by suspected release delay from the announced nuclear test by DPRK in 2013 [1]
We consider delayed release of up to 60 days
SRS (m-3)

## Slide 10
Challenges with Delayed Release
PTS-520
Prompt
Average number of fused events vs release delay, 2021
Release delay [days]
Allowing for delayed release significantly increases the number of fusion matches
Quickly becomes untenable to analyze such a large number of matches
Now investigating methods to rank fusion candidates based on information from multiple stations

## Slide 11
Future Work
PTS-520
The same waveform event may have matches with multiple RN stations
  Aligned SRS time series should agree on time of release
  The same nuclides should be measured at all stations
  Non-detections provide refuting evidence
Investigate a probabilistic model to incorporate information from non-detections
Investigate Bayesian inference models such as FREAR which incorporates non-detections and provides source location
  https://gitlab.com/trDMt2er/FREAR
SRS (m-3)

## Slide 12
PTS-520
Thank you!