## Slide 1
Design of an atmospheric radiotracer experiment to improve local-scale transport modeling
Carolyn Seifert1, Lynn Wood1, Michael Foxe1, Sean Stave1, Miles Bodmer2, Martin Keillor1, Christine Johnson1, James Ely1, Ethan Alger3, Michael Brown4, Elizabeth Dzenitis3, Akshay Gowardhan3, Derek Haas5, Clayton Hudson5, Gordon Macleod4, Michael Moore1, Rob Newsom1, Khiloni Shah5, Walter Schalk6, Sonia Wharton3
1Pacific Northwest National Laboratory
2Sandia National Laboratories
3Lawrence Livermore National Laboratory
4Los Alamos National Laboratory
5University of Texas at Austin
6National Oceanic and Atmospheric Administration
Presentation Date: 22 June 2023
O1.1-849

## Slide 2
Design large-scale experiments to meet LYNM science objectives
Build an experimental testbed at the Nevada National Security Site instrumented with >1000 sensors below ground and at the surface
Execute multiple experiments to capture multi-physics signatures
  Chemical explosions (3)
  Electromagnetic source (1)
  Atmospheric tracers (3)
Collect and archive data
The Low-Yield Nuclear Monitoring Program (LYNM) includes a testbed for integrated field experiments.
O1.1-849
This presentation: an atmospheric radiotracer transport experiment to improve local modeling.

## Slide 3
Flow Features Found in Complex Terrain
Complex terrain complicates near-field atmospheric transport of radionuclides, and empirical data are needed to inform and validate models.
O1.1-849
How does topography impact near-field atmospheric transport?
How do we optimize local radionuclide detection networks?
At what scale do local and regional atmospheric signatures converge?
To answer these questions, we designed a 5-km atmospheric radiotracer experiment:
Conduct 4 releases of 127Xe gas and smoke in a complex terrain
Deploy sensors up to 5 km downwind
  22 real-time NaI(Tl)-based radioxenon sensors
  11 meteorological stations + 1 surface energy flux tower + 1 daily radiosonde
  2 scanning lidars + 8 optical video cameras
Analyze whole air samples from up to 5 locations to validate real-time data

## Slide 4
A tracer release system was engineered to simultaneously emit smoke and radioxenon gas into the air.
O1.1-849
127Xe (half life of 36.4 days) was produced via irradiation of purified stable 126Xe in a research reactor
Remotely conducted four 127Xe releases, each ~550 MBq over 5 min
Smoke was produced using remotely ignited commercial smoke candles (>1700 m3/min for 5 min)
Aliquots of source gas were collected to validate source activity
127Xe and smoke releases were synchronized in time
Tracer release system during testing
Xe gas pressure and flow rate vs. time during one release

## Slide 5
A network of 22 real-time NaI(Tl) sensors was deployed to detect the radioxenon plume at distances up to 5 km.
O1.1-849
2L NaI(Tl) sensors packaged for field use
Sensors were remotely monitored via cellular network and cloud-based analysis software
Estimated 127Xe detection threshold at <10 Bq/m3 (via simulations)
Estimated source dilution factors of 10-9 to 10-8 at 5 km
Real-time counts in selected NaI(Tl) sensors
Deployed NaI(Tl) sensor
Sensor kits

## Slide 6
Radioxenon sensors were deployed in four arcs to capture plume crossing times up to 5 km away from two separate release points.
O1.1-849
Four arcs of Xe sensors out to 5km
Two scanning lidars in center of valley
10 met towers, surface energy flux tower, daily radiosonde release
Four releases from two locations: 127Xe + smoke
Cameras at release locations, on the hill, and downwind
Five whole air samplers co-located with Xe sensors
Apron 4
Apron 1

## Slide 7
A dense network of meteorological sensors was selected and deployed to measure local atmospheric properties.
O1.1-849
Release location
Scanning
lidars
Scanning lidars
Radiosondes
Meteorology (Met) towers
Energy flux tower
Video cameras

## Slide 8
Experiment was successfully conducted and data analysis is underway. Selected Xe sensor and lidar data are shown here from one release.
O1.1-849
Radial Velocity @ 10o
Backscatter @ 10o
Background-subtracted count rates observed in 20-220 keV region of interest for selected NaI(Tl) sensors
Lidar backscatter and radial velocity measurements (vertical slice)
Sensor locations where Xe was detected (green) and not detected (red)

## Slide 9
Whole-air samplers were designed to capture samples for later onsite and offsite laboratory analysis to confirm the real-time results.
O1.1-849
Samplers were programmed to collect at specified times after the release
Bottles were filled up to 80 psig (18 L) at collection time (~60 s to fill)
Whole-air samples were triaged onsite and later measured in a laboratory without and then with Xe separation
Some samples show detectable 127Xe in laboratory measurements
Data analysis continues…
Lab analysis results from whole air samples collected from one station from one 127Xe release
Whole air sampler
Sample bottle

## Slide 10
O1.1-849
This Low Yield Nuclear Monitoring (LYNM) research was funded by the National Nuclear Security Administration, Defense Nuclear Nonproliferation Research and Development (NNSA DNN R&D). The authors acknowledge important interdisciplinary collaboration with scientists and engineers from LANL, LLNL, NNSS, PNNL, SNL, UT, and NOAA.
Summary
Successfully designed and executed an atmospheric radiotracer experiment out to 5 km
Designed and deployed:
  Source release system
  Meteorological sensors
  Radioxenon sensors
  Whole air samplers
Performed four 127Xe + smoke releases over 3 days
Data analysis is still underway
Photograph of smoke release test