## Slide 1
Bayesian inversion of seismograms for source parameters of contained DPRK underground nuclear explosions
Anton Ziolkowski
University of Edinburgh
22 June 2023
02.1-326

## Slide 2
DPRK TEST SITE AND MDJ SEISMIC STN
Mudanjiang (MDJ) seismic station in China is 373 km north of
Punggye-ri nuclear test site in the Democratic People’s Republic of Korea (DPRK).

## Slide 3
DPRK TEST SITE AND MDJ SEISMIC STN
Mudanjiang (MDJ) seismic station in China is 373 km north of
Punggye-ri nuclear test site in the Democratic People’s Republic of Korea (DPRK).
From the seismograms recorded at MDJ, the goals are to recover
The source parameters and source time functions of the contained explosions
The Green’s function from the DPRK test site to MDJ.

## Slide 4: OUTLINE
Ox.x-xxx
Contained DPRK underground nuclear explosions
Method (Ziolkowski, 2022)
Blake’s 1952 source model
Inclusion of free surface and key parameters
Inversion by Very Fast Simulated Annealing (VFSA)
Results: Green’s functions to Mudanjiang (MDJ) seismic station
Results: Source time functions
Conclusions

## Slide 5: Relative epicenters constrained by InSAR-based ground displacement for 2016_01
2016_09
2009
2013
N
2016_01
Constrained by InSAR
Myers et al., SRL (2018)
Ellipses are 90%
probability areas
(Best Fit Gaussian)
2017_09
2006
Map View
Myers et al.,(SRL), 2018
Lawrence Livermore National Laboratory
LLNL-PRES-xxxxxx
5

## Slide 6: Seismograms recorded on common station are similar but variable amplitude
N
Myers et al., SRL (2018)
Ellipses are 90%
probability areas
(Best Fit Gaussian)
Lawrence Livermore National Laboratory
LLNL-PRES-xxxxxx
6
Signals at publicly available seismic station MDJ about 350 km north
DPRK 6 is ~ 10 X larger than DPRK 5
Trace normalized signals are similar
Time (seconds)
Time (seconds)
Myers (2019)

## Slide 7: DPRK 2 and DPRK 3: Detail
The seismograms are different in detail, caused by differences in the source time function.
For example, DPRK 2 is smaller and more high frequency than DPRK 3.

## Slide 8: METHOD
The contained explosions are all within about 1 km of each other.
The path from each explosion to the MDJ seismometer is the same.
The seismogram at MDJ for explosion is
We model and find its inverse filter from .
We estimate the Green’s function by convolving with :
We adjust the source parameters to minimise the differences among the different estimates of the Green’s function.

## Slide 9: BLAKE’S SOURCE MODEL
Blake replaced the nonlinear zone surrounding the explosion by a cavity of radius a with internal pressure
and placed it in a homogeneous isotropic elastic medium.

## Slide 10: BLAKE’S SOURCE MODEL
Blake’s 1952 model
At the boundary the pressure is
continuous.
Blake derived analytic expressions for the radial motion in the elastic zone, . The velocity potential
is velocity.
is reduced velocity potential (RVP).
is radiated pressure. is bulk modulus.
Blake replaced the nonlinear zone surrounding the explosion by a cavity of radius a with internal pressure
and placed it in a homogeneous isotropic elastic medium.
r
a
p0(t)
r, c, s

## Slide 11: INCLUSION OF FREE SURFACE
r
a
r, c, s
h
h
Virtual
Source
Free surface
p0(t)
Fundamental parameters to be found:
- resonant frequency
- Poisson’s ratio
- depth factor
- tensile strength of granite at radius a
All other parameters are derived from these parameters. Fracturing increases Poisson’s ratio and decreases P-wave velocity and tensile strength.
The virtual source introduces a reversed-polarity pressure wave with time delay :
Mount Mantap is a granite peak. We assume isotropy.
Density kg/m3.
Bulk modulus Pa.
Normally Poisson’s ratio is 0.25 .

## Slide 12: INVERSION WITH VFSA
In practice we use two sources, four parameters per source.
Very Fast Simulated Annealing (Sen, M. K. and P. L. Stoffa, 2013). For this problem:
  At each iteration each parameter is selected at random from its range;
  the source time functions are calculated,
  the Green’s functions are obtained by deconvolving the seismograms for the source time functions.
  the normalised root mean square difference (NRMSD) between the Green’s functions is the error.
  If the error is less than last time, we have a new model.
  If is greater we accept it with a reduced probability.
  At each iteration the temperature is gradually reduced.

## Slide 13: RECOVERED GREEN’S FUNCTIONS
Green’s functions:
All plotted on the same scale.
For the inversion seismograms were truncated just before the Rayleigh wave arrival. The recovered Green’s functions should all be the same. They are very similar, but not identical.

## Slide 14: GREEN’S FUNCTIONS: DETAIL
Seismograms
DPRK 2 & DPRK 3
Green’s functions
DPRK 2 & DPRK 3

## Slide 15: RECOVERED SOURCE TIME FUNCTIONS
Source time functions:
Individual scaling

## Slide 16: RECOVERED SOURCE TIME FUNCTIONS
Source time functions:
Equal scales

## Slide 17: RECOVERED SOURCE PARAMETERS

## Slide 18: NONLINEAR ZONES
Elastic radius (m)
DPRK 2 140
DPRK 3 220
DPRK 4 170
DPRK 5 250
DPRK 6 460

## Slide 19: NONLINEAR ZONES
Elastic radius (m)
DPRK 2 140
DPRK 3 220
DPRK 4 170
DPRK 5 250
DPRK 6 460

## Slide 20: NONLINEAR ZONES
Elastic radius (m)
DPRK 2 140
DPRK 3 220
DPRK 4 170
DPRK 5 250
DPRK 6 460

## Slide 21: NONLINEAR ZONES
Elastic radius (m)
DPRK 2 140
DPRK 3 220
DPRK 4 170
DPRK 5 250
DPRK 6 460

## Slide 22: NONLINEAR ZONES
Elastic radius (m)
DPRK 2 140
DPRK 3 220
DPRK 4 170
DPRK 5 250
DPRK 6 460

## Slide 23: NONLINEAR ZONES
Elastic radius (m)
DPRK 2 140
DPRK 3 220
DPRK 4 170
DPRK 5 250
DPRK 6 460

## Slide 24: CONCLUSIONS
We have extracted estimated source parameters and source time functions of the DPRK contained underground nuclear tests 2009-2017 from the seismograms recorded at Mudanjiang (MDJ) seismic station.
The recovered Green’s functions between the DPRK test site and MDJ are very similar, but not identical.
The recovered source time functions can be used to estimate Green’s functions to other seismometers.
The two 2016 tests DPRK 4 and DPRK 5 created weak fractured zones close to the site of DPRK 6, causing DPRK 6 to behave differently from the other explosions.

## Slide 25: Acknowledgments
I thank Steve Myers for permission to use slides from an excellent talk he presented in Edinburgh in 2019.
I thank many friends and colleagues with whom I have discussed this work over many years.
Finally, I thank the CTBTO for accepting this paper and for providing the funding to enable me to present it here.

## Slide 26: REFERENCES
Blake, F. G., 1952, Spherical wave propagation in solid media: Journal of the Acoustical Society of America, Vol. 24, No. 2, 211-215.
Myers, S. C., S. R. Ford, R. J. Mellors, S. Baker and G. Ichinose, 2018, Absolute locations of the North Korean Nuclear Tests Based on Differential Seismic Arrival times and InSAR: Seismological Research Letters, 89(6), 2049-2058.
Richards, P. G. and W.-Y. Kim, 2007, Seismic signature: nature physics | VOL 3 | JANUARY 2007 | www.nature.com/naturephysics.
Sen, M. K. and P. L. Stoffa, 2013, Global optimization methods in geophysical inversion: Cambridge University Press.
Ziolkowski, A., 2022, Explosive source signature determination: Two unequal shots in the same hole: Geophysical Prospecting, DOI: 10.1111/1365-2478.13251.