## Slide 1
Revisiting what a variety of tracers can tell about the occurrence of underground nuclear explosions
A. Pazdniakou1,V.V. Mourzenko2, J.-F. Thovert2, E. Pili3, P. M. Adler1
1Metis, Sorbonne Université, Paris, France
2Institut P', CNRS - Université de Poitiers - ISAE-ENSMA, Poitiers, France
2CEA, DAM, DIF, F-91297 Arpajon, France
Wien, June 2023
Objectives:
In addition to the traditional radioxenon, study several tracers such as H2O, radon, and CO2
possibly observe emissions of these additional tracers at the test site
possibly combine observation of radioxenon at the monitoring site
with observations of H2O and CO2 at the test site
Table of contents:
Configuration and modelization
Outputs at the nuclear test site: H2O and CO2
Outputs at the nuclear test site and at the monitoring site: 133Xe and Radon
4. Conclusion

## Slide 2
Configuration and modelization
Simplified structure:
Permeability: K=10-14 m2 porosity e= 0.29
T=802.15 K
3 initial pressures P0 =50, 100, 200 bars
Ground surface
Fracture network
Chimney
Cavity
Magma
Nuclear test site: Punggye-Ri nuclear test site (DPRK)
a parallelipipedon of size 200×200×650 m
Embedding porous medium:
Permeability Km=10-16 m2 porosity em = 0.01 or 0.05
192 or 384 fractures
aperture b = 1 mm
hexagons of radius R=20m
Fluctuating atmospheric pressure
period 105 s; amplitude 1000 Pa.
Patriarche et al, Stereological analysis of fractures in the Roselend tunnel and permeability determination.
Water Resources Research, 43: W09421

## Slide 3
Modelization: Pazdniakou et al. (2022), Two-Phase Flow, Heat and Mass Transfer and
Tracer Transport to the Atmosphere from Underground Nuclear Cavities
Through Fractured Porous Media. Pure and Applied Geophysics.
Porous medium
3D equations on the Darcy scale for flow, energy and tracer
Fractures
2D equations on the Darcy scale for flow, energy and tracer
plus exchanges with the surrounding porous medium
Numerical
- Meshing of the fractures (and all the bounding surfaces) by triangles, and of the porous medium by tetrahedra
- Discretization by the finite volume technique
- Solution by the conjugate gradient method
- Parallelization by OpenMP
Results:
at the test site (Punggye-Ri, DPRK) for an hypothetical 150 kt nuclear explosion, burried at 550 m
at the monitoring site (IMS JPX38-Takasaki, Japan):
includes a delay = 1 day and a dilution factor h = 7 10-18 s m-3
(see presentation O2.1-118 by Pili et al. on Thursday)

## Slide 4
2. Outputs at the nuclear test site
2.1. H2O
- Initial mass of water contained in the cavity  5000 T (sphere of radius 50 m; porosity 0.01)
To be compared with the 600 T contained in a standard
atmospheric column of 1000 m high above the test site, i.e. 15.5 g/m3
Mass flow rate
Detectable
by
satellite imaging?
Fractured porous medium with 192 fractures and porosity 0.05
Three initial cavity pressures after the collapse of the cavity roof and the formation of the chimney:
P0 = 50 bars 100 bars 200 bars
Total mass
transferred
to the atmosphere
Notes: comp_H20_1PHASE_PWORK_BG_T802.m
comp_M_H2O_BG_T802.png
comp_M_H2O_BG_T802_0_12h.png

## Slide 5
For P0 = 100 bars
Convention Porosity Number
of fractures
blue 0.05 192
red 0.01 192
black 0.05 384
broken red 0.01 384
Influence of the petrophysical properties of the surrounding medium
When the porosity decreases, the initial mass flow rate increases
When the number of fractures increases, the initial mass flow rate increases
Nuclear test site
Nuclear test site

## Slide 6
Comparison with an homogeneous model:
The fractured porous medium with e = 0.05 and Nf= 192 is replaced by an equivalent homogeneous medium:
permeability K=6.48 10-13 m2 and porosity =0.05 P0= 100 bars
Delay to fill in the porosity!

## Slide 7
Comparison between the fractured porous medium model (solid line)
and the homogeneous one (broken line): P0=100 bars e=0.05 Nf=192
Orders of magnitude conserved!

## Slide 8
2.2. CO2
Initially contained in a 10 m thick soil layer at the top of the medium
No fracture in this soil layer
Other properties of this layer:
permeability = 10-12 m2,
porosity = 0.3
Diffusion coefficient calculated according to Archie’s law
Mass flow rate at the ground surface: 300 mg/m2/hour
Initial mass fraction (corresponds to equilibrium): 7.6 10-2
No source term in these preliminary calculations

## Slide 9
CO2 mass Mc1 transferred to the atmosphere
Additional CO2 mass transferred to the atmosphere:
DMc1(t) = Mc1-mass transferred with no test
P0=
200 bars
100 bars
50 bars
atmospheric pressure fluctuations
Detectable
by
satellite imaging?
To be compared with
mass transferred to the atmosphere during 12 hours =144 kg

## Slide 10
Actually the tracer fluxes at the ground surface are very localized
though they are significantly smoothed out by the soil layer

## Slide 11
3. Outputs at the nuclear site and at the monitoring site
3.1. Radon
e = 0.01 Nf=192 P0 = 100 bars
Nuclear test site
Convention
Thin line = radon originated in the porous medium
Medium line = radon originated in the cavity
Thick line = sum
Notes: add_radon_xe_CTBO.m voir aussi add_radon_xe.m pour les figures complètes

## Slide 12
Desintegration number per 6 hours at the monitoring site:
delay = 1 day  t-1
l = 1.5428 10-6 s-1
h = 7 10-18 s m-3
Order of magnitude of the ambiant value  50 Bq/s  hopeless
Monitoring site with 6 hours sampling
Convention
Thin line = radon originated in the porous medium
Medium line = radon originated in the cavity
Thick line = sum
Notes: seq_C_CTBO_mm3_rplusxe_dm2.png

## Slide 13
3.2. 133Xe
Initially produced in the cavity: 1 mole, i.e. 133 g; dilution coefficient =7 10-18
e =0.05 Nf=192 fractures for the three values of P0
At the nuclear test site
At the monitoring site with 6 hours sampling
detection limit
MDC133Xe ~0,15 mBq/m3 for SAUNA III with a 6-hour sampling time (installed at JPX38), see Aldener et al. (2023)
~0,2 mBq/m3 for SPALAX NG with a 8-hour sampling time, see Topin et al. (2020).
1 mn
1h
1d
1 w
Notes: Pour le log_log 1 mole
comp_Bq_loglog_CEA_1PHASE_PWORK_BG_T802_1mole.m
comp_seq_C_CTBTO_Bq_BG_T802_1mole.png
comp_C_CTBTO_site_Bq_loglog_BG_T802_1mole.png
Pour le log_log: comp_Bq_loglog_CEA_1PHASE_PWORK_BG_T802.m donne comp_C_CTBTO_site_Bq_loglog_BG_T802.png
En linéaire: comp_Bq_CEA_1PHASE_PWORK_BG_T802.m donne comp_C_CTBTO_site_Bq_BG_T802.png et comp_seq_C_CTBTO_Bq_BG_T802.png

## Slide 14
4. Concluding remarks
- Radon cannot be detected at the monitoring site
- H2O and CO2 outbursts could possibly be detected at the test site by satellite imaging depending on sensitivity
One day later, 133Xe could be easily detected 1000 km away at the monitoring site considering the following scenario:
150 kt underground explosion at 550 m depth in a granitic rock
with a fracture network developed from the top of the chimney after cavity collapse