## Slide 1
The development of an association algorithm for radionuclide measurements
Paul Eslinger, Harry Miley, Brian Schrom
Pacific Northwest National Laboratory, USA
Presentation Date: dd June 2023
O3.6-364
This Low Yield Nuclear Monitoring (LYNM) research was funded by the National Nuclear Security Administration, Defense Nuclear Nonproliferation Research and Development (NNSA DNN R&D). The authors acknowledge important interdisciplinary collaboration with scientists and engineers from LANL, LLNL, NNSS, PNNL, and SNL.

## Slide 2
Goal: Implement a Radionuclide Data Pipeline that Focuses on Release Events rather than Samples using Data Fusion
IMS System
Spectrum and Analysis
Sample Flagged as L5/LC
IDC Algorithm and Lists
Sensitivity & Selectivity
Transport Parameter Calculations
Sample Automated RN Report
Sample Reviewed RN Report
Analyst Review
Detect Anomaly
Find Associated Samples
Estimate T0, Release Strength, Location
Includes local BKG
EVENT Bulletin 1
EVENT Bulletin 2
Waveform Fusion
Fused Event Bulletin
Bayesian Analyses
Analyst Review
O3.6-364

## Slide 3
What is ‘Sample Association’?
O3.6-364
1
2
3
5
6
7
Source of RN
RN Sample
Detectable Plume
Selecting the measurements to use in forming a release event
  Detect: 3 & 4
  Locate: 2, 3, 4, & 5
  Ignore: 1 & 6
Concept:
  Use air measurements from inside and near the plume to define the event
  Exclude measurements a long distance from the plume
4

## Slide 4
Summary and Status
O3.6-364
A first-generation automated association approach has been constructed
  Objectively selects neighbor samples in time and space
  Returns results quite similar to what an expert analyst would pick
This tool uses transport calculations averaged in some way…
  Full year of past air transport
  Current season for several years (e.g. Spring ‘20, Spring ’21, Spring ‘22)
  Custom period, such as last two weeks
The atmospheric transport model computations can be accumulated over time

## Slide 5
Computational Approach
O3.6-364
Approach
  Conduct a large set of atmospheric transport runs for RN sampling locations
    79 stations for one year (2014 meteorological data)
  Examine predicted detections at each station for a large number of possible release events spread across the globe
    Synthetic releases every 3 h for a year at 100,000 locations
  Build a huge matrix of “detect/not detect” status on all release events for every RN station
Define an “affinity” for plumes that pass over more than one station
  Given that station “A” has detected some subset of the releases, what fraction of those same releases are detected at station “B”?
  Can precompute and store “affinities” for each sampling location

## Slide 6
Example Affinity Results for ARP01
O3.6-364
Example calculations:
  Releases of 133Xe and current sampler detection limits
  The affinity value depends on the release magnitude
  Smaller releases have lower, more limited affinity
For large releases, stations that most often have detections from the same plume can be a long distance apart.
79 Station network

## Slide 7
Affinity Matches Expectations from Past Event Analysis
O3.6-364
Station Dis (km) Affinity (Name)
RUP58 1058 0.2463 Ussuriysk
JPP37 1518 0.2126 Okinawa
RUP60 2412 0.0931 Petropavlovsk
CNP20 2019 0.0454 Beijing
PHP52 2988 0.0439 Tenay
USP78 4157 0.0417 Midway
MNP45 2964 0.0391 Ulan Bataar
USP71 4950 0.0237 Sand Pt AK
RUP56 3210 0.0167 Peleduy
CNP22 2877 0.0166 Guangzhou
USP77 3284 0.0148 Wake Island
THP65 4603 0.0117 Bangkok
USP80 2595 0.0105 Guam
Example Affinity to JPX38 (Takasaki) for a 1013 Bq 133Xe Release Event
A. One detect
B. One detect, one non detect
C. Two detects
D. Three detects, two non detects
DPRK 2013

## Slide 8
Other Uses of the Affinity Data
O3.6-364
Approach
  Use the matrix of “detect/not detect” status on all releases for every sampler
  Compare common detections at pairs or groups of samplers
Build a map of detections that matches your detection rules
  Example: Detect release at RN74 but not at RN75
  How many of the 100,000 releases have consistent detections?

## Slide 9
A More Complex Joint-Association Example
Using Historical Meteorological Data
O3.6-364
Data Set
  Use the matrix of “detect/not detect” status on all releases for every sampler
Build a map of detections that matches your detection rules
  Releases every 3 h of 1013 Bq of 133Xe at 100,000 locations
  Noble gas detectors at RN20, RN38, and RN58
  How many releases are consistent with detections at RN38 but not RN20 or RN58?

## Slide 10
Conclusions
O3.6-364
A sample association approach has been constructed that can be automated for screening analyses
  Objectively selects neighboring samples in time and space
  Returns results quite similar to what an expert analyst would pick
  Uses averaged historical air movement
Once developed, the data matrix of “detection status” for release events becomes a lookup table
  Provides an initial selection of other samples an analyst might examine when evaluating a first detection
  Provides an initial look at possible source regions
The initial sample association is a launching point for analyst review

## Slide 11
Questions?
O3.6-364
Questions?