## Slide 1
Compilation of the latest evaluated decay data for the CTBT relevant and background radionuclides for γ-ray spectrometry
Chushiro YONEZAWA]
Japan Institute of International Affairs (JIIA)
The CTBT relevant RNs were selected around 2000, when the development of the verification system began, using decay data that were available at the time. More than 20 years have passed since that selection, and evaluated data are now available that are more reliable than the data at that time.
P3.6-066
From the DDEP, ENSDF, and IAEA evaluated attenuation data libraries, (1) two types decay data table of CTBT relevant RNs, (2) decay data tables of background RN for γ-ray spectrometry, (3) a list of γ-ray lines ordered by energy for CTBT relevant and background RNs, and (4) RN decay data tables used for calibration of γ-ray detectors were prepared.
Comparing the compiled data with the data used to select CTBT relevant RNs, the relative maximum differences in half-lives and primary γ-ray emission intensity, which have a significant impact on the accuracy of the radioactivity concentration, were large (10% and 36%, respectively), but the primary γ-ray energy was 0.1%.
Since the half-lives and γ-ray emission intensities between the compiled data and which used to select the CTBT relevant RNs significantly differ, and they directly affect the accuracy of the radioactivity measurement results, using of this compiled data is strongly recommended for the radioactivity measurement of RNs in IMS and OSI.
Please do not use this space, a QR code will be automatically overlayed

## Slide 2
1. Introduction
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
The CTBT relevant RNs were selected around 2000, when the development of the verification system began, using decay data that were available at the time1). However, now, more than 20 years after the selection was made, newly measured and further evaluated decay data with even higher reliability, evaluated by experts, are available. The author compiled the latest evaluated decay data (half-lives, decay modes and their branching probability, γ-ray energies and their emission intensities) for 96 RNs including the CTBT relevant RNs and short-lived RNs produced during their decay processes, and 49 natural RNs that may be observed as background in particulate monitoring by IMS, and prepared various data tables. The compiled decay data were compared with data used for the selection of the CTBT relevant RNs1).
The adopted evaluated decay data libraries are as follows:
Decay Data Evaluation Project (DDEP)2) : Preferentially adopted for this work
(2) Evaluated Nuclear Structure Data File (ENSDF)3): Adopted for RNs where no DDEP
(3) IAEA data for X Ray and Gamma Ray Decay Data Standards4): RNs for detector calibration
(4) Published data by Galan et al.5) for 135Xe

## Slide 3
2. Prepared decay data tables
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
Table 1 Summarized decay data for the CTBT relevant radionuclides (92 RNs, 5 pages)
Table 2 Detailed decay data for the CTBT relevant radionuclides (96 RNs, 52 pages)
Table 3 Detailed decay data for the background radionuclides in particulate monitoring (49 RNs, 27 pages)
Table 4 A list of γ-ray lines for CTBT relevant and background radionuclides ordered by energy (2090 lines, 61 pages)
Table 5 Decay data of radionuclides used for detector calibration (17 RNs, 5 pages)
Table 1
Table 2
Table 3
Table 4
Table 5

## Slide 4
3. Comparison of the compiled decay data with other
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
Comparison with the data used for selection of the CTBT relevant RNs (ref. 1)
Half-lives
Primary γ-ray energy
Primary γ-ray intensity

## Slide 5
3. Comparison of the compiled decay data with other
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
The top 10 RNs in order of relative differences
Half-life: 131mTe (9.77%), 108mAg (4.57%), 76As (1.42%), 187W (1.17%), 136Cs (1.15%), 196mAu (1.04%), 131mXe (1.02%), 97Zr (0.96%), 126Sb (0.89%), 132Te (0.80%).
Primary γ-ray energy: 156Sm (0.0980%), 127Sb (0.0890%), 106Rh (0.0410%), 57Co (0.0322%), 141Ce (0.0298%), 86Rb (0.0279%), 106mAg (0.0195%), 153Sm (0.0193%), 131mXe (0.0183%), 148Pm (0.0175%).
Primary γ-ray intensity : 131mTe (35.6%), 187W (17.8%), 91Y (15.4%), 105Rh (13.6%), 153Sm (7.57%), 129mTe (6.33%), 190Ir (4.80%), 127Sb (3.96%), 147Nd (3.15%), 152mEu (2.82%).
Summary of the results for the CTBT relevant RNs with ref. 1

## Slide 6
3. Comparison of the compiled decay data with other
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
Comparison of the OSI RNs with the data used for selection of CTBT relevant RNs (ref. 1)
Order of relative differences:
Half-life: 131mXe (1.02%), 132Te (0.80%), 133mXe (0.36%), 133Xe (0.084%), 137Cs (0.067%)
γ-ray energy: 141Ce (0.0298%), 131mXe (0.018%), 144Ce (0.011%), 133mXe (0.008%), 99Mo (0.008%)
γ-ray intensity: 147Nd (3.15%), 133Xe (2.70%), 144Ce (2.40%), 131mXe (1.65%), 133mXe (1.58%), 140Ba (0.85%)
Half-life
γ-ray energy
γ-ray intensity

## Slide 7
3. Comparison of the compiled decay data with other
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
Comparison between DDEP and IAEA data for RNs used for detector calibration
Other RNs than 226Ra (radioactive equilibrium state)
Half-life: <0.13%
γ-ray energy: <0.0012% γ-ray energy
γ-ray emission rate: <1.2%
Larger difference for 226Ra (radioactive equilibrium)

## Slide 8
4. Conclusions and References
P3.6-066
Please do not use this space, a QR code will be automatically overlayed
Compiled the latest evaluated decay data for the CTBT relevant RNs, background RNs, and detector calibration RNs.
The maximum relative difference of the compiled data from the data used for the selection of the CTBT relevant RNs: 10% (half-life), 0.1% (prim. γ-ray energy), 36% (prim. γ-ray).
The maximum relative difference between DDEP and IAEA data for detector calibration: 0.3% (half-life), 0.0076% (γ-ray energy), 1.25% (γ-ray emission intensity).
Since the half-lives and γ-ray emission intensities between the compiled data and which used to select the CTBT relevant RNs significantly differ, and they directly affect the accuracy of the radioactivity measurement results, using of this compiled data is strongly recommended for the radioactivity measurement of RNs in IMS and OSI.
References
1) L. -E. De Geer, Kerntecnik, 66, 113-120 (2001).
2) DDEP database, available from <http://www.lnhb.fr/ddep_wg/>, (accessed 2023-06-04).
3) ENSDF database, available from <https://www.nndc.bnl.gov/ensdf/> (accessed 2023-06-04).
4) IAEA, Update of X Ray and Gamma Ray Decay Data Standards for Detector Calibration and Other Applications, Volume 1 and 2, 2007.
5) M. Galan, M. Kalinowski, A. Gheddou, K. Yamba: J. Enviroment. Radioactivity 192 (2018) 628–634