## Slide 1
P3.6-99
Identical mother and daughter radionuclides related to CTBT for improving the detection of nuclear event
Sara Azimkhani
Atomic Energy Organization of Iran
Some fission products being on the standard list of CTBT relevant radionuclides, decay to radionuclides which are among the 83 CTBT relevant radionuclides.
The ratio of Lanthanum-140 to Barium-140, Technetium-99m to Molybdenum-99, Europium-156 to Samarium-156, Antimony-125 to Tin-125, Yttrium-91 to Strontium-91, Iodine-131 to Tellurium-131m, and Niobium-95 to Zirconium-95 has been calculated using Bateman equation for two scenarios:
      1. Fission radionuclide in daughter state
      2. Fission radionuclide in both mother and daughter states
Zero time of a nuclear event has been estimated for two given scenarios.