## Slide 1
P3.5-483
Azimuth Estimation in Seismic Arrays via Deep Augmented MUSIC
M. Khatib1, J . Merkofer2, Y. Ben-Horin3, Y. Radzyner3, G. Revach4, R. Sloun2, N. Shlezinger1, T. Routtenberg1,5
BGU1, Eindhoven University2, Soreq Nuclear Research Center3, ETH Zürich4, Princeton University5
DA-MUSIC - a hybrid MB/DD implementation of the MUSIC algorithm for DOA estimation.
The MUSIC algorithm is a well-regarded MB approach, and it exhibits inherent limitations
Enable DOA estimation with an unknown number of sources.
Achieve effective handling of broadband signals in the estimation process
Compare the performance of the hybrid MB/DD approach with both MB and DD benchmarks in low and high snapshot domains.
Demonstrate the remarkable resolution capability of the hybrid approach in various settings.
DD deep learning approaches offer robust DOA estimation yet are computationally intensive

## Slide 2
P3.5-483
Azimuth Estimation in Seismic Arrays via Deep Augmented MUSIC
M. Khatib1, J . Merkofer2, Y. Ben-Horin3, Y. Radzyner3, G. Revach4, R. Sloun2, N. Shlezinger1, T. Routtenberg1,5
BGU1, Eindhoven University2, Soreq Nuclear Research Center3, ETH Zürich4, Princeton University5
Covariance Recovery:
  Learning a surrogate covariance matrix to overcome limitations.
Number of sources estimation:
  Improving the number of sources estimation and categorization of noise eigenvectors.
Peak finding:
  Increase resolution and allow differentiation of entire structure.

## Slide 3
P3.5-483
Azimuth Estimation in Seismic Arrays via Deep Augmented MUSIC
M. Khatib1, J . Merkofer2, Y. Ben-Horin3, Y. Radzyner3, G. Revach4, R. Sloun2, N. Shlezinger1, T. Routtenberg1,5
BGU1, Eindhoven University2, Soreq Nuclear Research Center3, ETH Zürich4, Princeton University5
Training:
Gradient based optimization
Supervised learning
Judging a decision
– Permutation matrix
Advantages
Preserve flow of MUSIC
Enable end-to-end training
Overcome coherent sources
Improved resolutions
Increased robustness
Operate within low snapshots
Overcome broadband

## Slide 4
P3.5-483
Azimuth Estimation in Seismic Arrays via Deep Augmented MUSIC
M. Khatib1, J . Merkofer2, Y. Ben-Horin3, Y. Radzyner3, G. Revach4, R. Sloun2, N. Shlezinger1, T. Routtenberg1,5
BGU1, Eindhoven University2, Soreq Nuclear Research Center3, ETH Zürich4, Princeton University5
Non-Synthetic Data
Seismic data was collected using the GERES array, which comprises 25 vertical seismometers spaced about apart, with a total aperture of around .
The seismic signal at each sensor is sampled at . We use data from October to December of 2021, in which GERES detected arrivals for 2904 events: 2816 for analysis, 2534 for training and 282 for testing.
We employ sliding windows of length 100 seconds with a shift of 25 seconds around the signal arrival time.
 | DA-MUSIC | Broadband MUSIC | Classic MUSIC | Beam-former | Random
RMSPE | 0.6269 | 1.0075 | 1.2475 | 0.9383 | 1.7097
 | DA-MUSIC | Broadband MUSIC | Classic MUSIC | Beam-former | Random
 | 0.6269 | 1.0075 | 1.2475 | 0.9383 | 1.7097
DA-Music outperforms MB estimators by jointly focusing on frequency and interdependent elevation angle for a stable azimuth estimation.
Despite relatively large error, it’s important to consider the average error reported by the IDC Review Event Bulletin is