## Slide 1
The Multichannel Maximum-Likelihood Method: Towards a Multisource Detection and Wave Parameters Estimation Using Deep Learning
B. Poste1, M. Charbit2, A. Janela Cameijo1, A. Le Pichon1, C. Listowski1, F. Roueff2, J. Vergoz1
1 CEA, DAM, DIF, F-91297 Arpajon, France
2 Institut Mines-Telecom, 91120 Palaiseau
We present an improvement to the multichannel maximum-likelihood (MCML) method. The initially single source approach is extended to a multisource detection and wave parameters estimation algorithm.
P3.5-050
For this aim, several maxima on the likelihood function are selected in accordance to the likelihood amplitude and the errors on the maxima. The number of sources to select is fixed by a deep learning approach.
The results show that MCML is able to estimate several sources that are overlapping in the same time/frequency band cell. The deep learning allows MCML to select the correct number of maxima in the likelihood function.
To conclude the new improvement to the MCML algorithm allows the analyst to better characterize multiple simultaneous sources.
Please do not use this space, a QR code will be automatically overlayed

## Slide 2
Introduction: The recent improvement in infrasound array processing
P3.5-050
Please do not use this space, a QR code will be automatically overlayed
The MCML (Multi-Channel Maximum Likelihood) algorithm (Poste et al. 2022) has been implemented in order to deal with degraded recording conditions that can not be well resolved by PMCC (Progressive Multi-Channel Correlation).
MCML is implemented in the same time-frequency space as PMCC to validate the single-source hypothesis.
However this hypothesis does not hold in reality (figure below).
Thus a lower SNR signal can be hidden by another signal in the monosource implementation.

## Slide 3
Objectives: From monosource estimation towards a multisource use
P3.5-050
Please do not use this space, a QR code will be automatically overlayed
In the context of the CTBT, the objectives are :
To estimate the number of sources in the signal by a deep leaning method. AIC (Akaike Information Criteria) and BIC (Bayesian Information Criteria) tend to fail with low SNR that are typical of infrasound signals.
To generalize the MCML algorithm to the multisource case.
Velocity (m/s)
Velocity (m/s)
Azimuth (°)
Azimuth (°)

## Slide 4
Methods: The MCML algorithm and deep learning method
P3.5-050
Please do not use this space, a QR code will be automatically overlayed
MCML algorithm
Deep leaning method for source number estimation
The algorithm relies on a white and gaussian source assumption.
The estimation of the wavefront parameters is performed by the likelihood function computed on a (θ,v) grid.
A parabolic interpolation around the maximum on the grid is performed to avoid any accumulation at grid nodes.
The detection function is perfomed by the Generalized Likelihood Ratio (GLR).
A p-value threshold is implemented to discriminate noise from signal of interest on the basis of the GLR.
In the multisource case many maxima are selected. They are sorted in descending order of likelihood. Each maxima has an associated error. If the maximum i is included in the error of the maximum i-1, the maximum i is deleted.
The architecture used follows the work of Rogers (2021) on the estimation of radar sources.
This architecture uses as input, the covariance matrix of the signals with the associated eigenvalues in a vector: .
The architecture is a multiperceptron that stacks six sets of fully-connected layers, rectified linear unit, batch normalization and dropout layers. It ends with a softmax for multi-classes classification.
An adam optimizer and sparse categorical crossentropy loss function are used.
For each frequency bands and class (1 to 3 sources) studied there are 140 000 cases with SNR varying from -10 dB to 30 dB to simulate the SNR difference between both impulsive and permanent sources.
The data are split in 70% learning, 20% validation and 10% test. 500 epochs with 450 batchs of datas and a callback.
ReL
ReLu : activation function of dense layers.
Batch normalization : Stabilize the data across the network.
Dropout : Avoid overfitting by randomly silent connections.
Callback : Stop the learning if the validation loss function stagnates beyong 50 iterations.

## Slide 5
Results: Multisource estimations
P3.5-050
Please do not use this space, a QR code will be automatically overlayed
1st source : wind farms (yellow, orange), microbaroms (blue), Baikonur launch (green : 22h40-23h), wideband source (green), mining activity (light blue at high frequency).
The predictions are taken into account if the probability exceeds 95%, the number of sources is three otherwise.
2nd source
3rd source

## Slide 6
Conclusion
P3.5-050
Please do not use this space, a QR code will be automatically overlayed
To conclude, the MCML algorithm has been implemented by selecting multiple maxima of the likelihood function.
In order to avoid the selection of wrong maxima a deep learning method has been implemented to estimate the number of sources.
This method shows good results by avoiding the duplicate selection of high-SNR sources but the probability is still low in some cases, in particular at high frequency.
The ground truth is unknown that is why it’s difficult to verify real results.
On real signal the MCML has shown good results in particular the detection of overlapping permanent sources such as microbaroms.
An important task that remains to be done is to improve the detection algorithm to avoid the selection of false maxima that are counted to be real by the deep learning method and the p-value.

## Slide 7
References
P3.5-050
Please do not use this space, a QR code will be automatically overlayed
B. Poste and others, The multichannel maximum-likelihood (MCML) method: a new approach for infrasound detection and wave parameter estimation, Geophysical Journal International, Volume 232, Issue 2, February 2023, Pages 1099–1112, https://doi.org/10.1093/gji/ggac377.
Rogers, J., Ball, J. E., & Gurbuz, A. C. (2021). Robust estimation of the number of coherent radar signal sources using deep learning. IET Radar, Sonar & Navigation, 15(5), 431-440, https://doi.org/10.1049/rsn2.12047.