## Slide 1
Novel Portable Radioisotope Identification Device for Special Nuclear Material Detection and Characterization
M. Corbo, G. Mangiagalli, M. Morichi, I. Bonesso
CAEN SpA, Italy
NUCLEAR SECURITY
AND INSPECTION
TECHNOLOGY OVERVIEW
P3.3-471
NEUTRON IDENTIFICATION
CAPABILITIES
EXCEEDING THE REFERENCE
STANDARD
USE CASE SCENARIOS
Please do not use this space, a QR code will be automatically overlayed

## Slide 2
P3.3-471
Please do not use this space, a QR code will be automatically overlayed
INTRODUCTION: NUCLEAR SECURITY
AND INSPECTION
Passive detection systems are needed for nucelar security use, to maintain safety conditions and to avoid any interference with working procedures:
Fast response and short time measurement
Versatile and simple to use
Gamma detection/counting is the minimum requirement
Gamma Spectroscopy identification is an added value
Neutron detection/counting is a plus
Neutrons identification (Fast Neutrons) was not implemented until today

## Slide 3
P3.3-471
Please do not use this space, a QR code will be automatically overlayed
Passive detection systems used for security control in safety conditions and to avoid any interference with working procedures:
Fast response and Short time measurement
Versatile and simple to use
GAMMA detection/counting is the minimum requirement
GAMMA Spectroscopy identification is an added value
NEUTRON detection/counting is a plus
  NEUTRONS identification (FAST NEUTRONS) was not implemented until today
OBJECTIVES: TECHNOLOGY OVERVIEW
  GAMMA/NEUTRON COUNTING
  High-efficiency gamma/neutron organic detector
  Pulse Shape Discrimination algorithm
** same Pulse Shape Discrimination (PSD) implemented in the IAEA Fast Neutron Collar Monitor (fresh fuel verification) [2]
  GAMMA SPECTROSCOPY
  Equipped with mid-resolution (<4,0% @662 keV) gamma detector
  Peaks search in the spectrum to identify gamma nuclides
  Gamma peak search is used also in neutron source identification algorithm
  Enhance/correct the SNM identification
  Enrichment level estimation

## Slide 4
METHODS: NEUTRON IDENTIFICATION
CAPABILITIES
P3.3-471
Please do not use this space, a QR code will be automatically overlayed
Passive detection systems used for security control in safety conditions and to avoid any interference with working procedures:
Fast response and Short time measurement
Versatile and simple to use
GAMMA detection/counting is the minimum requirement
GAMMA Spectroscopy identification is an added value
NEUTRON detection/counting is a plus
  NEUTRONS identification (FAST NEUTRONS) was not implemented until today
NEUTRON SOURCE IDENTIFICATION
Different conditions:
Moderated
Shielded
Masked
Am/Be (red) area is discriminated through a 3rd parameter
International Patent Pending
PCT/IB2021/056349
Identification of mainly n emitting SNM (WGPu in lead box) + common gamma masking sources

## Slide 5
RESULTS: EXCEEDING THE REFERENCE
STANDARD
P3.3-471
Please do not use this space, a QR code will be automatically overlayed
ANSI N42.53 – 2013
Backpack Based Radiation Detection Systems Used for Homeland Security
  gamma alarm (4 ± 5%) photons/(cm2s) moving at 1,2 m/s @ 1m)
  2 s for neutron alarm (252Cf 20.000 n/s) moving at 1,2 m/s @1,5 m
  1 min or anything stated by the manufacturer to ID isotopes (GAMMA ONLY)
NEUTRON SOURCES: PU-239 75% ENRICHED
NEUTRON SOURCES: Cf-252, Am-Be
See reference [1]

## Slide 6
CONCLUSION: USE CASE SCENARIOS
P3.3-471
Please do not use this space, a QR code will be automatically overlayed
UNIQUE CAPABILITIES
Identification of mainly n emitting SNM (WGPu in a lead box) + common gamma masking source (I-131)
SCENARIOSES
Orphan source characterization
Search and ID of SNM in industrial facilities
Characterization of suspicious goods Characterization of legacy samples for destructive analysis
FAST ASSAY
PROMPT PREPARATION TO ACTION IN CASE OF SNM DETECTION

## Slide 7
REFERENCES
P3.3-471
Please do not use this space, a QR code will be automatically overlayed
[1] Special Nuclear Material Identification Through One-Minute Measurement with a New Backpack Radiation Device in Real Scenario Conditions, https://doi.org/10.18280/ijsse.110416
[2] Beaumont, J.S., Lee, T.H., Mayorov, M. et al. A fast-neutron coincidence collar using liquid scintillators for fresh fuel verification. J Radioanal Nucl Chem 314, 803–812 (2017). https://doi.org/10.1007/s10967-017-5412-x