## Slide 1
Natural and artificial Ar-37/Ar-39 signatures in the underground
Roland Purtschert & Stéphanie Musy
Climate and Environmental Physics and
Oeschger Center for Climate Change Research,
University of Bern, Sidlerstrasse 5, 3012, Bern, Switzerland
In the case of a UNE, 39Ar and 37Ar are produced by activation reactions on rocks. Because of their different half-lives, the 37Ar/39Ar ratio is a function of the timescale of production (pulsed vs. continuous), the depth-dependent production mechanisms, and the Ca/K ratio of the rocks.
P3.3-458
37Ar and 39Ar measurements of 80 groundwater samples in different lithologies were compiled [1]. The measured ratios were compared with theoretical calculations including neutron and muon reactions [2]
Calculated production - and measured 37Ar/39Ar activity ratios for different rock types agree reasonably well, indicating secular production-decay-equilibrium. Pulsed UNE production would result in activity ratios that are three orders of magnitude higher.
37Ar/39Ar activity ratios after an UNE in different rock types can now be better estimated and assessed.
Please do not use this space, a QR code will be automatically overlayed
37Ar and 39Ar measurements of 80 groundwater samples in different lithologies were compiled [1]. The measured ratios were compared with theoretical calculations including neutron and muon reactions [2]

## Slide 2
Introduction
P3.3-458
Please do not use this space, a QR code will be automatically overlayed
Natural soil samples were collected from a drill core from an alluvial valley in Switzerland. The samples were irradiated with a known neutron flux and emanated Ar-37 was determined
In the case of a UNE, 37Ar and 39Ar are produced in the rock matrix by neutron activation of Ca and K, respectively [1].
The natural 37Ar and 39Ar production rates in rocks are dominated by the same reactions but are also affected by muon-induced reactions. They depend therefore on the depth below the surface [2].
Calculated 37Ar/39Ar natural activity ratios were compared to ratios measured in groundwater samples [3] in different rock formations
The 37Ar/39Ar ratio in the subsurface is a function of the timing of the production (i.e. pulsed vs. continuous), production mechanisms, and the rock composition (mainly Ca/K ratio)
The 37Ar/39Ar ratio can therefore be used as a conclusive indicator of whether a measured 37Ar/39Ar signature is from a recent or ancient UNE, or is from natural origin.

## Slide 3
Objectives
P3.3-458
Please do not use this space, a QR code will be automatically overlayed
Comparison and differentiation of natural 37Ar/39Ar ratios with expected UNE signatures
Verification of the calculated 37Ar/39Ar ratios by means of measured ratios
Characterisation of natural 37Ar/39Ar signatures in different rocks as function of depth underground

## Slide 4
Methods
P3.3-458
Please do not use this space, a QR code will be automatically overlayed
Relevant production reactions:
39Ar in sandstone as an example
Depth depended production ratios
b) The Ca/K normalized natural production ratios:
-vary mostly where m- capture reactions are relevant
are relatively uniform in greater depths (0.2-0.5)
are similar to ratios resulting from a Watt neutron spectra
Dominance of
39Ar | 37Ar
Neutron (N) activation reactions | 
39K(N,p)39Ar | 40Ca(N,α)37Ar
42Ca(N,α)39Ar | 39K(N,P2N)37Ar
Muon capture reactions | 
40Ca(µ-,p )39Ar | 39K(µ-,2N)37Ar
39K(µ-,γ)39Ar | 40Ca(µ-,p2N)37Ar
Stopping m- reactions
Fast m induced neurons
a) The production ratios 37Ar/39Ar(prod) depend on rock composition and vary as function of depth. Colours indicate main production reaction vs. depth
39Ar production in a Sandstone as function of depth for the production reactions considered (Left side).
a)
b)
[4]

## Slide 5
Results
Comparison with data from groundwater
P3.3-458
Please do not use this space, a QR code will be automatically overlayed
Measured 37Ar/39Ar activity concentrations in old groundwater samples agree reasonably well with the calculated productions activities (i.e. production-decay equilibrium due to the prolonged residence- and production time underground)
The highest natural 39Ar activities observed in groundwater are about 5 dpm/LAr
Pulsed production (i.e. UNE) results in 37Ar/39Ar activity ratios three order of magnitude higher (factor l37/l39)
UNE 37Ar/39Ar activity ratios decay to natural values as a function of time but with residual 39Ar compared to natural levels (> 5dpm/LAr)
37Ar/39Ar activity ratios that are above natural ratios at sites with elevated 39Ar activities inform about the timing of the test carried on.
37Ar -39Ar activity concentrations (decays per min per L Argon) measured in deep ( > 100 m) groundwaters. Green area: calculated production ratios [2] ; Orange area: elevated activity concentration after a UNE as a function of time (red labels).
High-Ca rocks (Limestones)
Sandstones
Crystalline rocks

## Slide 6
Conclusions and References
P3.3-458
Please do not use this space, a QR code will be automatically overlayed
Natural 37Ar/39Ar production rate ratios in different rock types and as a function of depth have been calculated
The results are in accordance with activity ratios values measured in gas extracted from old groundwater
Activity ratios after a UNE are expected to be three orders of magnitude higher than natural levels (i.e. ~5000), depending on the rock type surrounding the cavity.
The comparison of measured 37Ar/39Ar ratios and 39Ar activity concentrations with calculated values might be a diagnostic tool for OSI measurements.
References
[1] McIntyre, J.I., et al., (2017) Measurements of Argon-39 at the U20az underground nuclear explosion site. Journal of Environmental Radioactivity 178-179, 28-35.
[2] Musy, S. and Purtschert, R. (2023) Reviewing Ar-39 and Ar-37 underground production in shallow depths with implications for groundwater dating. Science of The Total Environment, 163868.
[3] Purtschert, R. and Althaus, R. (2012) Ar-39 dating of groundwater: How limiting is underground production?, Goldschmidt Conference, Montreal, p. p22f.
[4] Šrámek, O., Stevens, L., McDonough, W.F., Mukhopadhyay, S. and Peterson, R.J. (2017) Subterranean production of neutrons, Ar-39 and Ne-21: Rates and uncertainties. Geochimica et Cosmochimica Acta 196, 370-387.