## Slide 1
Development and Validation of Coincidence Analysis/Quantification
Software for Gamma-gamma Coincidence Counting
Manish Sharma, Jonathan Burnett
Pacific Northwest National Laboratory
Multidimensional systems promising for IMS
A Sophisticated γ-γ Coincidence Analysis/Quantification Software developed at Pacific Northwest National Laboratory, USA
P3.2-360
Advanced python libraries and strategies implemented
Experimental validation using underground γ-spectrometer
Probabilities simulated using PNNL’s Deception Supercomputer
Experimentally tested up to 120 GB experimental data
CTBT relevant radionuclides probabilities simulated
Coincidence probabilities validated: <5% for 15 radionuclides
Successful development and performance evaluation
Execution tested for CTBT relevant radionuclides
Experimental validation for 15 radionuclides
Place your QR Code here after removing this text box!
Disclaimer: The views expressed here do not necessarily reflect the views of the United States Government, the United States Department of Energy, the National Nuclear Security Administration or the Pacific Northwest National Laboratory.

## Slide 2
Abstract
Place your QR Code here after removing this text box!
P3.2-360
Gamma-gamma coincidence techniques are known to improve the detection of particulate radionuclides relevant for Treaty monitoring purposes. To that end, Pacific Northwest National Laboratory (PNNL, USA) has developed a novel γ-γ coincidence analysis and radionuclide quantification software package. The software’s execution has been tested for radionuclides relevant to Comprehensive Nuclear-Test-Ban Treaty (CTBT) and other radionuclides with complex decay schemes. This presentation discusses software’s details, challenges encountered in its development, and its experimental validation. The validation was performed by experimentally measuring 15 radionuclides (including 140Ba, 140La, and 88Y) using the Advanced Radionuclide Gamma-spectrOmeter (ARGO) located in the Shallow Underground Laboratory (SUL) at PNNL.

## Slide 3
Introduction
Place your QR Code here after removing this text box!
P3.2-360
Radionuclide (RN) monitoring: one of four verification technologies of the IMS
IMS: RN stations utilize high-resolution gamma spectrometry for particulate radionuclides
  Such as: 140La, 140Ba, 134Cs, 137Cs, etc.
Multidetector systems promising for IMS:
  Superior detection efficiency
  - Coincidence signatures
  Operationally resilient
Additional detectors bring complexity
  Data processing, analysis, and quantification sophisticated software
  Mathematical operations, Nuclear Structure, Characterized source-detector geometry
M. Sharma et al., SnT-2021

## Slide 4
Software-I: Coincidence Analysis
Time delay AnaLysis using binAry SearcH (TALASH)
Place your QR Code here after removing this text box!
P3.2-360
Schematic of a ‘dual-detector’ system
TALASH development constraints:
        Implementation: Windows, Python, TLIST (Canberra)
        Output: Genie-2000
Large data problem (high count rate/time)
M. Sharma, J. Burnett, “Development and Performance Evaluation of a Novel - Coincidence Analysis Software,” NIM-A (2023, in press).

## Slide 5
Place your QR Code here after removing this text box!
P3.2-360
Software-I: Coincidence Analysis
Performance Optimization
Performance Optimization with Synthetic Data
Sophisticated Strategies
Large Data Chunking - optimization
M. Sharma, J. Burnett, “Development and Performance Evaluation of a Novel - Coincidence Analysis Software,” NIM-A (2023, in press).
Memory Utilization during Coincidence Search

## Slide 6
Place your QR Code here after removing this text box!
P3.2-360
Software-I: Coincidence Analysis
TALASH: Output (GUI)
TALASH Output
Coincidence pairs
Singles/Summed spectra
Coincidence spectra
TALASH - GUI
TALASH – Output (HDF5)
TALASH – Sample Delay Histogram
M. Sharma, J. Burnett, “Development and Performance Evaluation of a Novel - Coincidence Analysis Software,” NIM-A (2023, in press).
In Progress!

## Slide 7
Software-2: Radionuclide Quantification using 𝜸-𝜸 Signatures
Overview and Modules
Place your QR Code here after removing this text box!
P3.2-360
Strategies:
        Python, multiprocessing implementation
        Modular structure to reduce computational burden
Archived - cascades for CTBT-relevant radionuclides - PNNL’s Deception Supercomputer

## Slide 8
Validation Results
Place your QR Code here after removing this text box!
P3.2-360
Radionuclide | Coincidence Energy (keV) |  |  |  |  | (%)
 | Gated | Observed |  | Experiment | Simulated | 
60Co | 1173.2 | 1332.5 |  | 6.5E-4 | 6.3E-4 | 2.6
88Y | 1836.1 | 898.0 |  | 5.6E-4 | 5.6E-4 | 0.3
99Mo | 181.1 | 739.5 |  | 3.7E-4 | 3.7E-4 | 0.8
132Te | 228.2 | 49.7 |  | 3.3E-3 | 3.2E-3 | 1.2
140Ba | 162.7 | 304.8 |  | 4.9E-4 | 4.9E-4 | 0.5
140La | 1596.0 | 328.0 |  | 2.6E-4 | 2.6E-4 | 0.3
103Ru | 53.3 | 557.1 |  | 2.7E-5 | 2.8E-5 | 3.2
143Ce | 57.4 | 293.3 |  | 1.1E-3 | 1.1E-3 | 1.2
140La | 1596.0 | 328.0 |  | 2.6E-4 | 2.6E-4 | 0.2
42K | 1524.6 | 312.6 |  | 6.8E-6 | 6.5E-6 | 4.2
97Zr | 254.2 | 1148.0 |  | 1.7E-5 | 1.7E-5 | 0.0
132I | 522.7 | 772.6 |  | 2.2E-4 | 2.2E-4 | 0.2
133I | 706.6 | 529.9 |  | 3.4E-5 | 3.3E-5 | 0.8
131I | 80.2 | 284.0 |  | 4.8E-4 | 4.9E-4 | 1.0
153Sm | 103.2 | 69.7 |  | 7.0E-4 | 7.0E-4 | 0.4
Radionuclide | Coincidence Energy (keV) |  |  |  |  | 
 | Gated | Observed |  | Experiment | Simulated | 
60Co | 1173.2 | 1332.5 |  | 6.5E-4 | 6.3E-4 | 2.6
88Y | 1836.1 | 898.0 |  | 5.6E-4 | 5.6E-4 | 0.3
99Mo | 181.1 | 739.5 |  | 3.7E-4 | 3.7E-4 | 0.8
132Te | 228.2 | 49.7 |  | 3.3E-3 | 3.2E-3 | 1.2
140Ba | 162.7 | 304.8 |  | 4.9E-4 | 4.9E-4 | 0.5
140La | 1596.0 | 328.0 |  | 2.6E-4 | 2.6E-4 | 0.3
103Ru | 53.3 | 557.1 |  | 2.7E-5 | 2.8E-5 | 3.2
143Ce | 57.4 | 293.3 |  | 1.1E-3 | 1.1E-3 | 1.2
140La | 1596.0 | 328.0 |  | 2.6E-4 | 2.6E-4 | 0.2
42K | 1524.6 | 312.6 |  | 6.8E-6 | 6.5E-6 | 4.2
97Zr | 254.2 | 1148.0 |  | 1.7E-5 | 1.7E-5 | 0.0
132I | 522.7 | 772.6 |  | 2.2E-4 | 2.2E-4 | 0.2
133I | 706.6 | 529.9 |  | 3.4E-5 | 3.3E-5 | 0.8
131I | 80.2 | 284.0 |  | 4.8E-4 | 4.9E-4 | 1.0
153Sm | 103.2 | 69.7 |  | 7.0E-4 | 7.0E-4 | 0.4
PNNL’s Advanced Radionuclide Gamma spectrOmeter-I
Validation of Detection Probabilities (Experiment vs Software)

## Slide 9
Conclusions
Place your QR Code here after removing this text box!
P3.2-360
Development of sophisticated coincidence analysis/quantification software at PNNL
  Performance evaluation and optimization
Software’s execution tested for CTBT relevant radionuclides (and complex decay radionuclides, 233U)
  Validated with experimental measurement of 15 radionuclides (using calibration standards and irradiated samples)
What’s not discussed, but has been done:
  Comparison with existing software (AWE’s RIMMER)
  Impact of interferences (own/other emissions)
  Convergence behavior for 15 radionuclides
  Further details on experimental probability calculation and comparison

## Slide 10
Place your QR Code here after removing this text box!
P3.2-360
Thank You!