## Slide 1
Distributed Acoustic Sensing: A Step Towards the Standardization
Kislov K.V.1, Gravirov V.V.2
1 Institute of Earthquake Prediction Theory and Mathematical Geophysics (IEPT RAS)
2 The Schmidt Institute of Physics of the Earth (IPE RAS)
DAS has been experiencing exponential development, but still there are many challenges. [1]. In our opinion, the main problems are metrological. The aim is no longer to improve individual parameters, the research in this direction successfully continues. At present, it is necessary to develop a comprehensive and united set of these parameters, to standardize the methods of their description, to standardize the process of preparing works, measurements and presentation of data [2]. A lot of work in this direction was done in preparation for the Global DAS monitoring month February 2023 [3].
P3.1-175
This particular research involved data manufactured by T8 Sensor, LLC connected to approx. 700 m shallow buried cable, operated by Sternberg Astronomical Institute, Moscow State University and located in Northern Caucasus, approx. 20 km to the South from the city of Kislovodsk [5].
A standard optical cable containing a dark fiber was buried under a loose soil layer, i.e. laid on a rocky base at a depth of 25-30 cm.
The uniformity of the cable, the uniformity of its laying along the entire length of the line, and the same ground conditions gave us hope that the metrological characteristics would be approximately the same along the cable.
By analyzing the data obtained during the Global DAS monitoring month, we, first of all, took care to compare the seismic signals that came from different azimuths. To do this, the cable was divided into conditionally straight sections. The arrival azimuths of seismic waves at each site were determined.
This allowed us to determine how much the signal level was affected by local geological conditions along the propagation paths of seismic waves and by the orientation of different sections of the cable.
The maximum angle between the individual parts of the cable was 110 degrees, so the effect of the location of the sensitivity axis of the individual virtual sensors should be significant.
Then we compared the signals amplitudes of different channels, which had to have a similar response.
A comparison of signals from different azimuths to differently located cable sections showed that the amplitude response depends significantly less on the angle of incidence of the seismic wave on the cable axis than it was estimated by calculations. First, this may be due to geological conditions along the wave propagation, second, due to bends and turns of the cable inside the GL, and third, due to the fact, that the optical fiber was coiled around the cable core.
The amplitude response of the signals from different channels turned out to be very different. And most often, neighboring or nearby channels had a similar type of response. This suggests that minor changes in cable laying conditions have an impact on the transfer function.
Initial estimates of DAS metrological characteristics of already laid communication cables cannot satisfy most requirements, therefore they are useless. We are not sure whether only this type of cable, such ground conditions and this method of laying the cable, create this effect. But, most likely, this is true for all cases of using a communication cable. Thus, the metrological characteristics for each cable should be determined separately (before, during or after the measurements).
To implement features of DAS to the fullest possible extent you can use special fibers and their careful laying. However, such cables are much more expensive, and special method of laying them is required. That is, one of the main advantages of DAS disappears. In addition, the use of special fibers does not completely eliminate metrological problems [7].
Please do not use this space, a QR code will be automatically overlayed

## Slide 2
Introduction
P3.1-175
Please do not use this space, a QR code will be automatically overlayed
DAS has been experiencing exponential development, but still there are many challenges. [1]. In our opinion, the main problems are metrological. The aim is no longer to improve individual parameters, the research in this direction successfully continues. At present, it is necessary to develop a comprehensive and united set of these parameters, to standardize the methods of their description, to standardize the process of preparing works, measurements and presentation of data [2]. A lot of work in this direction was done in preparation for the Global DAS monitoring month February 2023 [3].

## Slide 3
Objectives
P3.1-175
Please do not use this space, a QR code will be automatically overlayed
Initially, it was assumed that knowing the characteristics of the fiber optic cable, soil properties and cable laying conditions, it was possible to a priori estimate some of the main metrological characteristics of the DAS system, such as transfer function, noise level, etc. [4]. This would allow the full use of DAS data straight away after connecting the interrogator to a communication fiber line, and it is also possible in real time.

## Slide 4
Methods/data
P3.1-175
Please do not use this space, a QR code will be automatically overlayed
The uniformity of the cable, the uniformity of its laying along the entire length of the line, and the same ground conditions gave us hope that the metrological characteristics would be approximately the same along the cable.
By analyzing the data obtained during the Global DAS monitoring month, we, first of all, took care to compare the seismic signals that came from different azimuths. To do this, the cable was divided into conditionally straight sections. The arrival azimuths of seismic waves at each site were determined.
This allowed us to determine how much the signal level was affected by local geological conditions along the propagation paths of seismic waves and by the orientation of different sections of the cable.
The maximum angle between the individual parts of the cable was 110 degrees, so the effect of the location of the sensitivity axis of the individual virtual sensors should be significant.
Then we compared the signals amplitudes of different channels, which had to have a similar response.
Splitting the cable line into straight sections (kindly provided by
Yu. Starovoit).
This particular research involved data manufactured by T8 Sensor, LLC connected to approx. 700 m shallow buried cable, operated by Sternberg Astronomical Institute, Moscow State University and located in Northern Caucasus, approx. 20 km to the South from the city of Kislovodsk [5]. A standard optical cable containing a dark fiber was buried under a loose soil layer, i.e. laid on a rocky base at a depth of 25-30 cm.

## Slide 5
Results
P3.1-175
Please do not use this space, a QR code will be automatically overlayed
A comparison of signals from different azimuths to differently located cable sections showed that the amplitude response depends significantly less on the angle of incidence of the seismic wave on the cable axis than it was estimated by calculations. First, this may be due to geological conditions along the wave propagation, second, due to bends and turns of the cable inside the GL, and third, due to the fact, that the optical fiber was coiled around the cable core.
The amplitude response of the signals from different channels turned out to be very different. And most often, neighboring or nearby channels had a similar type of response. This suggests that minor changes in cable laying conditions have an impact on the transfer function.
Signals of Earthquakes from different azimuths.

## Slide 6
Conclusion
P3.1-175
Please do not use this space, a QR code will be automatically overlayed
Initial estimates of DAS metrological characteristics of already laid communication cables cannot satisfy most requirements, therefore they are useless. We are not sure whether only this type of cable, such ground conditions and this method of laying the cable, create this effect. But, most likely, this is true for all cases of using a communication cable. Thus, the metrological characteristics for each cable should be determined separately (before, during or after the measurements).
To implement features of DAS to the fullest possible extent you can use special fibers and their careful laying. However, such cables are much more expensive, and special method of laying them is required. That is, one of the main advantages of DAS disappears. In addition, the use of special fibers does not completely eliminate metrological problems [7].
Seismograms: above – Gaziantep, Turkey Δ ~ 850 km, M 7,8; middle – Murghab, Tajikistan Δ ~ 2700 km, M 6,8;
bottom – local noise.

## Slide 7
References
P3.1-175
Please do not use this space, a QR code will be automatically overlayed
Kislov K.V., Gravirov V.V. Distributed acoustic sensing: a new tool or a new paradigm // Seismic Instruments. 2022. V. (5). P. 485–508. DOI: 10.3103/S0747923922050085
Nikitin S.P., Kislov K.V., Starovoit Yu.O., Bengalsky D.M., Spiridonov E.P., Kharasov D.R., Fomiryakov E.A., Naniy O.E., Treshchikov V .N. Opportunities and prospects for the use of distributed fiber optic sensors in geophysics // Instruments and Experimental Techniques. (in press).
Kislov K.V., Nikitin S.P. Teleseismic monitoring "Global Distributed Acoustic Sounding Month": experience, current state and trends // Proceedings of the VII International Scientific and Practical Conference "Fundamental and applied aspects of geology, geophysics and geoecology using modern information technologies". Republic of Adygeya, Maykop. 2023. Part 1. P. 155 – 165. (in Russian)
Kislov K.V., Gravirov V.V. Acquisition of Seismological Data Using Fiber Optic Communication Lines // XIV International Conference and School “Problems of Geocosmos–2022”, St. Petersburg State University, St. Petersburg, Petrodvorets, Russia, 2022. GC2022-SG008.
Nikitin S., Treshchikov V. Global DAS month experiment, T8_Sensor-Caucasus dataset // International Federation of Digital Seismograph Networks. Dataset/Seismic Network. 2023. https://doi.org/10.7914/t8my-dk69
Jousset P., Wuestefeld A., Krawczyk C., Baird A., Currenti G., Landrø M., Nowacki A., Spica Z., Barajas S.R., Lindner F., Konca Ö.A., Edme P., Lai V.H., Treshchikov V., Urmantseva L., Morten J.P., Lienhart W., Lipovsky B.P., Schoenball M., Ma K.-F. and the “DAS-month” team (sample only!): Global Distributed Fibre Optic Sensing recordings of the February 2023 Turkey earthquake sequence., EGU General Assembly 2023, Vienna, Austria, 24–28 Apr 2023, EGU23-17618, https://doi.org/10.5194/egusphere-egu23-17618, 2023.
Kislov K.V., Gravirov V.V. Regarding the Metrology of Special Lines of the Distributed Acoustic Sensing // XIV International Conference and School “Problems of Geocosmos–2022”, St. Petersburg State University, St. Petersburg, Petrodvorets, Russia, 2022. GC2022-SG009.