## Slide 1
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Akiko FURUNO, Yutaka TOMITA, Toshiyuki KURIHARA, Yoichi YAMAMOTO, Ryuta Ohmori, Yuya Minakawa
Japan Atomic Energy Agency
We focus on Cs-137 detected at the Okinawa station (JPP37), which is located on an island in the Pacific Ocean and has no nuclear facilities nearby, and estimate the release source using IMS data and ATM analysis.
P2.4-547
For all days when Cs-137 was detected in JPP37:
Check the weather map
Check if Cs-137 was detected at stations other than JPP37
Back-tracking for 5 days from the day Cs-137 was detected
Season of detection is mostly from Dec. to May high correlation with CNP20 and MNP45
Backtracking simulations show that plume migration to these stations are relatively well reproduced
Possible release areas are Mongolia - inland China
Place your QR Code here after removing this text box!
We organized the Cs-137 detections in the East Asia region. It was possibly related to the Yellow-sand phenomenon. We would like to continue monitoring and analysis in this region.

## Slide 2
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Place your QR Code here after removing this text box!
Introduction
We are responsible for data analysis and management of IMS radionuclide monitoring stations as the NDC of Japan
There are two IMS radionuclide monitoring stations in Japan, at Takasaki for particles and noble gases and at Okinawa for particles
The detection frequency of Cs-137:
Takasaki Station
（RN38）
Okinawa Station
（RN37）
AS054
IS30
PS22
AS053
AS051
AS052
AS055
Mutsu TXL-2
(MUX88)
Horonobe TXL-3
(JPX81)
Takasaki (JPP38): high
originating mainly from the Fukushima Dai-ichi
Nuclear Power Plant Accident
Okinawa (JPP37) : occasionally, release source is unknown
  An island in the Pacific Ocean with no nuclear facilities in the vicinity
  Affected by long-range dispersion?
P2.4-547
TXL: Transportable Xenon Laboratory

## Slide 3
Place your QR Code here after removing this text box!
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Objectives
focus on Cs-137 detection at Okinawa (RN37)
clarify the characteristics of the season and the pressure pattern of each detection
back-trajectory analysis using an atmospheric transport model will be conducted to estimate the release source of Cs-137, by comparing with the IMS data including the surrounding stations
 | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Total
2012 |  |  |  | 1 |  |  |  |  |  |  |  |  | 1
2013 |  |  |  |  |  |  |  |  | 1 |  |  |  | 1
2014 |  |  |  |  |  |  |  |  |  |  |  |  | 
2015 |  |  |  |  |  |  |  |  |  |  |  |  | 
2016 |  |  |  |  |  |  |  |  |  |  |  |  | 
2017 |  |  |  | 1 |  |  | 5 |  |  | 1 |  | 3 | 10
2018 | 1 | 2 |  | 8 |  | 1 | 1 | 1 |  |  |  |  | 14
2019 |  |  |  |  | 2 |  |  |  |  |  |  |  | 2
2020 |  |  |  | 7 | 5 |  |  |  | 1 | 1 | 1 | 2 | 17
2021 | 1 | 3 |  | 2 |  | 1 |  |  |  |  |  |  | 7
Total | 2 | 5 | 0 | 19 | 7 | 2 | 6 | 1 | 2 | 2 | 1 | 5 | 
Number of days Cs-137 was detected at RN37
Frequency of detection has increased since 2017
Highest frequency is in April, also frequently detected from December to May
Need to confirm detection in July-August
P2.4-547

## Slide 4
Place your QR Code here after removing this text box!
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Methods/Data
Check the weather map
Check if Cs-137 was detected at stations other than JPP37
Back-tracking for 5 days from the day Cs-137 was detected
For all days when Cs-137 was detected in JPP37:
Model：HYSPLIT (NOAA)
Input Meteorological data：GDAS 1.0°
Validation data: IDC RRR
Tracer : Cs-137
Release rate and duration: 1 Bq/hour for 24 hours
Period of analysis：2012 – 2021
Number of the tracer particles：100,000
Vertical diffusion：Kanthar/Clayson
Horizontal diffusion：determined as ratio of the vertical diffusion
Simulation conditions of the back-tracking:
P2.4-547

## Slide 5
Place your QR Code here after removing this text box!
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Results
(1) Percentage (%) of detections at nearby stations within 5 days prior to the date of detection of Cs-137 at JPP37
 | Dec.-Feb. | Mar.- May | Jun.-Aug. | Sep.-Nov
CNP20 | 75.0 | 57.7 | 11.1 | 40.0
CNP21 | 16.7 | 46.2 | 11.1 | 0.0
CNP22 | 8.3 | 30.8 | 0.0 | 20.0
JPP38 | 41.7 | 65.4 | 88.9 | 60.0
MNP45 | 16.7 | 84.6 | 0.0 | 0.0
RUP56 | 8.3 | 30.8 | 11.1 | 0.0
RUP58 | 16.7 | 23.1 | 0.0 | 20.0
RUP60 | 16.7 | 15.4 | 11.1 | 0.0
JPP37
JPP38
CNP22
CNP21
CNP20
MNP45
RUP56
RUP58
RUP60
CNP20 makes a large contribution from December to May
MNP45 contributes significantly only from March to May
8 Yellow-sand observation days to western Japan out of 26 MAM detection days
P2.4-547

## Slide 6
Place your QR Code here after removing this text box!
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Results
(2) Percentage of Cs-137 detection dates at nearby stations coinciding with the date the plume arrived by backtracking
 | DJF | MAM | JJA | SON
CNP20 | 75.0 | 50.0 | 0.0 | 50.0
CNP21 | 16.7 | 11.5 | 0.0 | 0.0
CNP22 | 0.0 | 7.7 | 0.0 | 0.0
JPP38 | 0.0 | 3.8 | 0.0 | 33.3
MNP45 | 16.7 | 57.7 | 0.0 | 0.0
RUP56 | 0.0 | 0.0 | 0.0 | 0.0
RUP58 | 0.0 | 7.7 | 0.0 | 0.0
RUP60 | 0.0 | 0.0 | 0.0 | 0.0
JPP37
JPP38
CNP22
CNP21
CNP20
MNP45
RUP56
RUP58
RUP60
Backtracking results show that in most cases from December to May, the radioactive plume reached northern China (CNP20) to near Mongolia (MNP45) or the continental interior
There were no stations where the plume reached during the summer season
P2.4-547

## Slide 7
Place your QR Code here after removing this text box!
P2.4-547
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Results
(3) Typical example when Cs-137 was detected in spring at JPP37:
14 May 2020
 | CN20 |  | CN21 |  | JP37 |  | MN45 | 
 | Sim. | Obs. | Sim. | Obs. | Sim. | Obs. | Sim. | Obs.
14 May | 0 |  | 0 |  | 0.38925 | 3.69 | 0 | 
13 May | 0 | 11.66 | 0 |  | 0.02919 |  | 0 | 
12 May | 0.00037 | 16.90 | 0 |  | 0 |  | 0 | 2.97
11 May | 0.0003 | 14.47 | 3.4E-06 |  | 0 |  | 0.00206 | 
10 May | 3.4E-05 | 1.93 | 1.4E-05 |  | 0 |  | 0.00268 | 
H
L
L
0:00UTC 14 May
from ‘Kishojin’
https://kishojin.weathermap.jp/diary.php?ym=202004
Possible release source: Mongolia – inland China (Yellow sand?)
24h
48h
72h
96h

## Slide 8
Place your QR Code here after removing this text box!
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Results
P2.4-547
(4) Typical example when Cs-137 was detected in summer at JPP37:
21 July 2017
 | JP37 |  | JPP38 | 
 | Sim. | Obs. | Sim. | Obs.
21 Jul | 0 | 3.68 | 0 | 
20 Jul | 0 |  | 0 | 
19 Jul | 0 |  | 0 | 
18 Jul | 0 |  | 0 | 4.30
17 Jul | 0 |  | 0 | 
L
L
L
H
H
0:00UTC 21 July
Possible release source:???
Peak energy: 660.94keV
Reference energy: 661.66keV
FWHM= 2.49 (1.66) keV
: Possibility of false positives detection
Spectrum analysis results
from ‘Kishojin’
https://kishojin.weathermap.jp/diary.php?ym=201707

## Slide 9
Place your QR Code here after removing this text box!
Characteristics and sources of Cs-137 detected at IMS radionuclide monitoring stations in Japan
Conclusion
JPP37 is an island in the Pacific Ocean where Cs-137 is sometimes detected despite the fact that there are no nuclear facilities on the island or nearby
Season of detection is mostly from December to May
  High correlation with CNP20 throughout that period and with MNP45 from March to May => possibly related to the Yellow-sand phenomenon
Backtracking calculations show that plume migration to CNP20 and MNP45 is relatively well reproduced
Possible release areas are Mongolia - inland China
The typical meteorological pattern in spring that Cs-137 detection in Okinawa is a high-pressure system is overhanging from the continent
Possible release areas of cases detected in summer is unknown
P2.4-547