## Slide 1
Modelling wet deposition to improve test-ban monitoring
Stijn Van Leuven1,2,3, Pieter De Meutter1,2, Johan Camps1, Piet Termonia2,3 & Andy Delcloo2,3
1SCK CEN, 2Royal Meteorological Institute of Belgium, 3Ghent University
The simulation of wet deposition of radionuclides in atmospheric transport modelling (ATM) remains uncertain due to the parameterisation schemes used in simulations.
P2.4-654
We explore a new method to optimise the efficiency of the wet scavenging processes in ATM.
Our method improves the modelling of wet deposition, while being very computationally inexpensive.
This can enhance the quality of source reconstruction in the context of test-ban monitoring.
Please do not use this space, a QR code will be automatically overlayed
Improvement of model-observation correspondence
● before ● after

## Slide 2
►
INTRODUCTION
P2.4-654
Please do not use this space, a QR code will be automatically overlayed
Atmospheric transport modelling (ATM) is crucial for source reconstruction in the context of test-ban monitoring
Wet deposition is one of the main contributors to depletion of particulate radionuclides from the atmosphere
Scavenging is exponential decay process
Scavenging by
ice nucleation
snow collection
rain collection
cloud condensation nucleation
ATM used in this study Flexpart v10.4
 | - | activity concentration []
 | - | scavenging coefficient []
 | - | timestep []
 | - | 
 | - | 
 | - | 
 | - | rain intensity []
 | - | particle diameter (distribution) []
 | - | 
 | - | 

## Slide 3
OBJECTIVES
P2.4-654
Please do not use this space, a QR code will be automatically overlayed
[µBq/m³]
Fukushima nuclear power plant incident (2011)
137Cs transport and deposition
Measurements from International Monitoring System (IMS)
Case study
The simulation of wet deposition in ATM remains uncertain due to the parameterisation schemes used in simulations
In Flexpart this uncertainty can be captured in the scavenging parameters (, , , )
We explore a new method to optimise the efficiency of these parameters, which should improve wet deposition modelling in ATM
◄ Default scavenging in Flexpart overestimates activity air concentration by a factor ~6

## Slide 4
METHODOLOGY
P2.4-654
Please do not use this space, a QR code will be automatically overlayed
1
3-step systematic framework
▼ Simulation for IMS station RN71
Define the contributions of individual scavenging processes (, , , ) for each measurement:
Apply appropriate scaling scheme to scavenging processes:
3
Minimise cost function by varying ’s:
▲ minimisation in 4D parameter space (schematic example)
2

## Slide 5
METHODOLOGY
RESULTS
P2.4-654
Please do not use this space, a QR code will be automatically overlayed
▲ Simulation for IMS station RN71
▲ Simulation for IMS station RN71
▲ Measurements vs. default model
▲ Measurements vs. optimised model
Before
Removes bias between observations and model
Scaling factor for all scavenging processes increased
Due to compensating effects, the relative contribution of some processes can decrease despite the above
After

## Slide 6
CONCLUSION
P2.4-654
Please do not use this space, a QR code will be automatically overlayed
The proposed optimisation scheme is able to improve model-observation correspondence by scaling the wet scavenging contributions of the different scavenging processes
This method is much more efficient than a brute force method, as it only requires one simulation
Improving the modelling of wet deposition in ATM can aid CTBT monitoring by enhancing the quality of source reconstruction
paper (pre-print): Van Leuven, S., De Meutter, P., Camps, J., Termonia, P. and Delcloo, A., 2023, An optimisation method to improve modelling of wet deposition in atmospheric transport models: applied to FLEXPART v10.4, EGUsphere, https://doi.org/10.5194/egusphere-2023-357