## Slide 1
P2.4-215
Detection and Analysis of Anomalous Radioxenon Isotopes
Michael Mayer, Matthew Cooper, James Ely, Paul Eslinger,
Michael Foxe, James Hayes, Justin McIntyre, Mark Panisko
Pacific Northwest National Laboratory Richland, WA USA
Newly observed isotopes suggest new source of interfering xenon background (scientific research facilities)
  Neutron irradiation and spallation facilities can produce and release xenon
New isotopes interfere with all traditional ROIs used for activity calculations
  Algorithms will continue to calculate normally, but concentrations and ratios will not make sense
  125I might cause issues with 133Xe activity concentration due to its long half-life if there is a large amount in the detector
Xenon International observed new xenon isotopes while undergoing system testing in Knoxville, TN
  Next generation radioxenon system
  Better sensitivities and larger Xe volume than current systems
Isotopes of xenon were observed to be 125Xe, 127Xe, and 129mXe, and 122Xe
  125Xe and 122Xe both decay down to a radioactive iodine.
This Ground-based Nuclear Detonation Detection (GNDD) research was funded by the National Nuclear Security Administration, Defense Nuclear Nonproliferation Research and Development (NNSA DNN R&D).
PNNL-SA-186132