## Slide 1
P2.3-398
Christoph Pilger, Peter Gaebler, Andreas Steinberg, Johanna Lehr
Federal Institute for Geosciences and Natural Resources (BGR)
Systematic event analysis of IMS hydrophones
to identify and categorize hydroacoustic sources
Machine Learning based Denoising
Example: one year of IMS
hydroacoustic data (H08S)
We apply a machine learning based denoising approach on IMS hydrophone waveform data to reduce continuous noise sources and highlight transient features (DPRK’s 6th nuclear test and earthquake P-waves)
Proof of concept: large improvement of signal-to-noise-ratio, good transferability and generalization
Main conclusion: more specialized training could selectively remove noise sources and highlight events of CTBT interest, thus supporting waveform analysis and improving source identification and classification