## Slide 1
Development of Automatic Procedures for Selecting Samples Associated with a Release Event Based on the Evolution Consistency of Isotopic Ratios
Joshua Kunkle, Boxue Liu, Yuichi Kijima, Robin Schoemaker, Jolanta Kuśmierczyk-Michulec, Martin Kalinowski
CTBTO
Isotopic Ratios are used to associate samples to common origins
P2.1-521
Samples having anomalous concentrations are selected, filtered, and matched using Atmospheric Transport Modeling
Sample sequences are created for further analysis and creation of Possible Source Regions
Future work will expand the procedure to include event discrimination and timing
Please do not use this space, a QR code will be automatically overlayed

## Slide 2
Expert Technical Analysis using Isotope Ratios
P2.1-521
Please do not use this space, a QR code will be automatically overlayed
Algorithms And Associated Hypothesis Testing Applied to Noble Gas Spectrum Analysis Results and Event Characterization Regarding CTBT-Relevant Nuclear Events, Liu et.al.
Isotope ratios are utilized instead of activity concentrations to eliminate the variability due to atmospheric transport
If the source location and type is known, the predicted isotope ratios at IMS stations vary only as a function of time due to differing half-lives
Measured activity concentration ratios between
Xe-133 and Xe-131m for the release from the suspected 2013 DPRK nuclear test
This poster presents an automatic processing pipeline that associates samples based on the evolution of activity ratios

## Slide 3
Enable Expert Technical Analysis through automatic sample selection and association
P2.1-521
Please do not use this space, a QR code will be automatically overlayed
Example analysis period from station RN63 in December 2022
  Focus on radioxenon isotopes : Xe-131m, Xe-133, Xe-133m, Xe-135
Identify seeds samples where at least 2 Xenon isotopes are detected with anomalous concentrations
Form sequences based on time-interval requirements
Level A – no detection
Level B – detection
Level C – anomalous detection
RN63 observes frequent anomalous detections due to nearby civil facilities

## Slide 4
Seed selection and Sequence generation
Px.x-xxx
Please do not use this space, a QR code will be automatically overlayed
Level A – no detection
Level B – detection
Level C – anomalous detection
Trim non-interesting samples
Combine sequences having overlapping seeds
Sample sequences are further qualified by checking consistency among all measurements

## Slide 5
Connection Through Atmospheric Transport Modeling
P2.1-521
Please do not use this space, a QR code will be automatically overlayed
ATM backward simulation from RN63 at T – 115h
RN63
As radioisotopes are transported through the atmosphere, they may pass other IMS stations, or the same IMS station multiple times
The IDC produces ATM backwards simulations corresponding to each sample measurement
  Predicts particle concentration vs location and time
  Current resolution is 1 hour, 0.5 x 0.5 deg
  Tracing is performed for up to 14 days in the past
If the ATM simulation suggests that samples may be relate, they are joined into the same sequence

## Slide 6
Sample association
P2.1-521
Please do not use this space, a QR code will be automatically overlayed
Selected samples at station RN63
The seed sample having the smallest uncertainties is chosen as defining
Samples are associated using a 2-sided t-test, having 5% probability of rejecting true association
Results are saved for further interactive analysis

## Slide 7
Next Steps
P2.1-521
Please do not use this space, a QR code will be automatically overlayed
Possible Source Region Determination from ATM simulations – see poster P{2.4-334 by Robin Schoemaker
Event Discrimination
  Automatically determine source of event
  Utilize data and simulations of Nuclear Power Plant releases and Nuclear Explosions
Event timing
  Determine most likely release time based on event discrimination results