## Slide 1
Ambient Noise During Nyepi in Denpasar
I Putu Dedy Pratama, Pande Komang Gende Arta Negara, Dwi Karyadi Priyanto
Meteorologycal, Climatologycal, Geophysical Agency of Indonesia
Nyepi day, rest the Bali island for one day from anthropogenic noise
P1.2-078
Short Period seismometer installed to monitor ambient noise before, on, and after Nyepi day
Nyepi day decreased the anthropogenic noise
The Nyepi Day affects ambient noise in Denpasar City
Please do not use this space, a QR code will be automatically overlayed

## Slide 2
Introduction : Nyepi The Unique Tradition in Bali
P1.2-078
Please do not use this space, a QR code will be automatically overlayed
Catur Brata Penyepian ( 4 Nyepi rules): Amati Geni (no fire/light), Amati Karya (no work), Amati Lelungan (no go outside), Amati Lelanguan (fasting and no entertainment) for 24 hour start at 6 am local time
Nighttime satellite imageries for Nyepi Day 2021
Nyepi Day
After Nyepi Day
Before Nyepi Day

## Slide 3
Objectives of the research
P1.2-078
Please do not use this space, a QR code will be automatically overlayed
Denpasar City is the area that changes the most significantly from human activity during Nyepi.
Denpasar is an area with a population density of 7,412 people/km2 which is almost 10 times the population density of the Bali Province.
For this reason, it is necessary to conduct research on changes in human activity during Nyepi in Denpasar City.
Using Short Period Seismometer TDS DS04-A

## Slide 4
Methods and Data used for Nyepi Ambient Noise Measurement
P1.2-078
Please do not use this space, a QR code will be automatically overlayed
The H/V graphic snippet at 18:00 WITA on the day (a) before, (b) during, and (c) after Nyepi shows that the HVSR analysis using Geopsy has the reliability criteria and the overall peak of the curve is met.
The HVSR curve is obtained by comparing the horizontal component (SH) spectrum to the vertical component (SV) spectrum. Explicitly the HVSR method satisfies the equation :
The seismic vulnerability index (Kg) is a parameter that can be used to determine the level of vulnerability of an area to the threat of earthquake risk.

## Slide 5
Results of Ambient Noise for Nyepi Day
P1.2-078
Please do not use this space, a QR code will be automatically overlayed
The measurement point at the Denpasar Geophysics Station has Kg> 6 which is included in the high zone. This is in accordance with the geology of the measurement point which is located in a layer of clay sediment because previously it was a rice field area.

## Slide 6
Conclusion of Nyepi Impact on Ambient Noise
P1.2-078
Please do not use this space, a QR code will be automatically overlayed
The Nyepi Day increases the dominant frequency value and decreases the amplification factor in Denpasar City at the Denpasar Geophysics Station point. The Nyepi Day affects ambient noise in Denpasar City.
The seismic vulnerability index decreased during Nyepi by 3,906 compared to the average of the days before and after Nyepi.
For microtremor measurements that minimize the vibration factor of human activity outside of Nyepi Day, it should be done at 23:00-06:00 Local Time.

## Slide 7
References
P1.2-078
Please do not use this space, a QR code will be automatically overlayed
R. D. Borcherdt, Effects of Local Geology on Ground Motion near San Francisco Bay, Bull. Seismol. Soc. Am. 60, 1970, p.29–61.
Y. Nakamura, A Method for Dynamic Characteristics Estimation of Subsurface using Microtremor on the Ground Surface, Quarterly Report of RTRI, 30:1, 1989, p.25-33.
A. Panou, N. Theodulidis, P. Hatzidimitriou, et al., Reliability of Ambient Noise Horizontal-to-Vertical Spectral Ratio in Urban Environments: The Case of Thessaloniki City (Northern Greece). Pure appl. geophys. 162, 2005, 891–912, https://doi.org/10.1007/s00024-004-2647-6.
Y. Nakamura, On The H/V Spectrum, The 14th World Conference on Earthquake Engineering October 12-17, 2008, Beijing, China.
M. Nogoshi,& T. Igarashi, On the Amplitude Characteristics of Microtremor (Part 2), J. Seismol. Soc. Japan 24, 1971, p.26–40.
M. Herak, Model HVSR—A Matlabs Tool to Model Horizontal to Vertical Spectral Ratio of Ambient Noise. Computers Geosciences, 2008, p.1514–1526.
U. N. Prabowo, Pemetaan Tingkat Resiko Gempa Bumi Berdasarkan Data Mikrotremor Di Kotamadya Denpasar, Bali, Jurnal Kurvatek; 1(2), 2017, p.55-59.