## Slide 1: Quantifying atmospheric uncertainty and detection quality impacts on infrasound localization
Infrasound Technology Workshop (ITW2024)
Philip Blom1, Jordan Bishop1, & W. Garth Frazier2
1Los Alamos National Laboratory
2NCPA, University of Mississippi
LA-UR-24-31074
This Ground-based Nuclear Detonation Detection (GNDD) research was funded by the National Nuclear Security Administration, Defense Nuclear Nonproliferation Research and Development (NNSA DNN R&D). This work was supported by the U.S. Department of Energy through the Los Alamos National Laboratory.

## Slide 2
Back Projection Localization
Examples
  Multi-phase single-station localization
  Regional multi-station localization
Localization Confidence Trends
Summary and Ongoing R&D
Outline

## Slide 3
Background – Auxiliary Parameters
The equations defining rays in an inhomogeneous, moving atmosphere are:
  , ,
Auxiliary parameters defining variations with respect to the initial inclination and azimuth angles can be introduced to solve the Transport equation, ,
Additional differential equations are defined by taking derivatives of the above,
Auxiliary parameters were originally investigated to solve the transport equation, define geometric losses, and identify caustics (Blom & Waxler, 2012)

## Slide 4
Background – Auxiliary Parameters
The equations defining rays in an inhomogeneous, moving atmosphere are:
  , ,
Auxiliary parameters defining variations with respect to the initial inclination and azimuth angles can be introduced to solve the Transport equation, ,
Additional differential equations are defined by taking derivatives of the above,
Auxiliary parameters were originally investigated to solve the transport equation, define geometric losses, and identify caustics (Blom & Waxler, 2012)

## Slide 5
Background – Auxiliary Parameters
Auxiliary parameters were subsequently leveraged as part of a Levenberg-Marquardt eigenray algorithm
The Jacobian determinant is used in weakly non-linear waveform evolution computations
,

## Slide 6
Back Projection Localization
During discussions with Garth Frazier at Ole Miss NCPA, the idea came up to use the auxiliary parameters in a back projection localization algorithm
General idea:
  Infrasound stations (arrays) detect an event providing coherence (SNR) and direction-of-arrival information (back azimuth and trace velocity)
  Compute time-reversed ray path for each detected phase and use the auxiliary parameters to quantify the probability of a source at a hypothetical location and origin time, producing that detection when the spatial point doesn’t lie along the ray path.

## Slide 7
Back Projection Localization
Considerations:
  Implemented auxiliary parameters are only spatial. Can we define variation of propagation time along the ray path? (not included here, see manuscript)
  How can we quantify uncertainty/confidence in detection direction-of-arrival estimates?
  Localization should include uncertainty in the atmospheric state, but avoid introducing many parameters (e,g., EOF coefficients)?
During discussions with Garth Frazier at Ole Miss NCPA, the idea came up to use the auxiliary parameters in a back projection localization algorithm
General idea:
  Infrasound stations (arrays) detect an event providing coherence (SNR) and direction-of-arrival information (back azimuth and trace velocity)
  Compute time-reversed ray path for each detected phase and use the auxiliary parameters to quantify the probability of a source at a hypothetical location and origin time, producing that detection when the spatial point doesn’t lie along the ray path.

## Slide 8
Back Projection Localization – Ray Tracing
Time-reversed ray tracing requires swapping the wind flow direction (east ⬌ west, north ⬌ south)
In spherical geometry, the inclination angles at launch and arrival are different, so reciprocity is a bit more complicated (but still valid)
 | Eigenray | Time-Reversed Projection
Starting Location | 30°, -110° | 30°, -105.5°
Arrival Location | 30°, -105.4998° | 29.9999°, -110.0002°
Launch Inclination | 9.32190589° | 9.3168453°
Arrival Inclination | 9.3168453° | 9.32190589°
Launch Azimuth | 88.893277° | -88.85578°
Arrival Back Azimuth | -88.85578° | 88.893263°
Propagation Time | 1484.417 sec | 1484.425 sec
Transport Coefficient (rel. 1 km) | -43.1139 dB | -43.1138 dB

## Slide 9
Back Projection Localization – Likelihood
The likelihood defines the probability of observing a detection in the case that a given source hypothesis is true,
The ray path solution defines the various values, and the auxiliary parameters relate variations in the launch angles to those in , for example,
…we just need to define and

## Slide 10
Back Projection Localization – Uncertainty
Previous likelihood construction defined a relation between an azimuthal probability distribution function (von Mises) and the Fisher statistic (SNR) of the detection:
Expanding for small differences, ,
  Detection with : °

## Slide 11
Back Projection Localization – Uncertainty
Expanding for small differences, ,
  Detection with : °
Assuming the distribution is symmetric in slowness space, trace velocity variance is similarly defined:
  Detection with :
Previous likelihood construction defined a relation between an azimuthal probability distribution function (von Mises) and the Fisher statistic (SNR) of the detection:

## Slide 12
Relating trace velocity to inclination angle requires knowledge of the ambient sound speed, so uncertainty in that quantity must also be considered

  Detection with , :
Some complications at shallow angles when the denominator grows large, but the physical constraint of can be used to limit
Back Projection Localization – Uncertainty

## Slide 13
A synthetic event has been constructed to evaluate the back projection method
Standard deviations along the time-reversed paths exhibit reasonable behavior
Latitude and longitude variations increase at nearly constant rate with propagation range
  note: propagation to the southwest, so increased ray length left to right in figure
  At 40° latitude, 0.2° ~17 km
Propagation time uncertainty is on the order of 10’s of seconds and increases like latitude/longitude
Caustics near the turning heights show up in
Back Projection Localization – Uncertainty

## Slide 14
The formulation thus far uses a single atmospheric specification:
Quantify uncertainty by considering an atmospheric ensemble:
Note: atmospheric sounding application:
Back Projection Localization – Atmo Uncertainty
Atmospheric perturbation ensembles computed using stochprop software (see Blom et al., 2023)

## Slide 15
Example – Single-Station Multi-Phase Detections
Tropospheric and stratospheric phases were identified at St George during the FSE explosions
A localization estimate has been computed for FSE-2 using tropospheric and slow stratospheric phases
95% confidence region of 5400 km2
 | Ground Truth | Back Projection
Location | 37.221°, -116.061° | 37.224°, -116.030°
Origin time | 20:06:00 | 20:06:06
, , | - | 13.8 km, 20.1 km, 63 sec
 | Ground Truth | Back Projection
Location | 37.221°, -116.061° | 37.224°, -116.030°
Origin time | 20:06:00 | 20:06:06
 | - | 13.8 km, 20.1 km, 63 sec

## Slide 16
Example – Multi-Station Regional Detections
Synthetic event was constructed using a reference set of stations in the western US
  Source at Utah Test and Training Range (UTTR)
  Stations DLIAR (LANL), PDIAR (Pinedale, WY), and NVIAR (Mina, NV)
Propagation times and direction-of-arrival information computed using eigenray analysis
Detection JSON file constructed usable in InfraPy BISL and in-development back-projection localization methods
Notes: Note: cropping dims:
convert Figure_1.png -crop 548x340+35+80 test.png

## Slide 17
Example – Multi-Station Regional Detections
Synthetic event was constructed using a reference set of stations in the western US
  Source at Utah Test and Training Range (UTTR)
  Stations DLIAR (LANL), PDIAR (Pinedale, WY), and NVIAR (Mina, NV)
Propagation times and direction-of-arrival information computed using eigenray analysis
Detection JSON file constructed usable in InfraPy BISL and in-development back-projection localization methods
Notes: Note: cropping dims:
convert Figure_1.png -crop 548x340+35+80 test.png

## Slide 18
Example – Multi-Station Regional Detections
Synthetic event was constructed using a reference set of stations in the western US
  Source at Utah Test and Training Range (UTTR)
  Stations DLIAR (LANL), PDIAR (Pinedale, WY), and NVIAR (Mina, NV)
Propagation times and direction-of-arrival information computed using eigenray analysis
Detection JSON file constructed usable in InfraPy BISL and in-development back-projection localization methods
Notes: Note: cropping dims:
convert Figure_1.png -crop 548x340+35+80 test.png

## Slide 19
Example – Multi-Station Regional Detections
BISL lacks crosswind corrections, so the estimated source is displaced in the direction of the stratospheric winds (cross wind impact is underestimated)
Back projection methods produce a more accurate estimate and reduce area of the 95% confidence ellipse (2200 km2 vs. 8100 km2)
 | Ground Truth | BISL | A0 | 5 m/s uncertainty | 10 m/s uncertainty
Location | 41.131°, -112.896° | 41.351°, -111.98° | 41.138°, -112.847° | 41.190°, -112.827° | 41.194°, -112.835°
Origin time | 12:06:00 | 12:08:02 | 12:06:14 | 12:06:24 | 12:06:23
, , | - | 20.6 km, 20.9 km, 83 sec | 10.6 km, 11.2 km, 38 sec | 11.2 km, 11.2 km, 36 sec | 15.0 km, 12.2 km, 43 sec
 | Ground Truth | BISL | A0 | 5 m/s uncertainty | 10 m/s uncertainty
Location | 41.131°, -112.896° | 41.351°, -111.98° | 41.138°, -112.847° | 41.190°, -112.827° | 41.194°, -112.835°
Origin time | 12:06:00 | 12:08:02 | 12:06:14 | 12:06:24 | 12:06:23
 | - | 20.6 km, 20.9 km, 83 sec | 10.6 km, 11.2 km, 38 sec | 11.2 km, 11.2 km, 36 sec | 15.0 km, 12.2 km, 43 sec

## Slide 20
Localization Confidence Trends
There are minimal differences between the A0 estimate and that obtained for m/s
This implies that uncertainty introduced by finite detection SNR (f-stat = 25) dominates compared with that introduced by this atmospheric uncertainty
 | Ground Truth | BISL | A0 | 5 m/s uncertainty | 10 m/s uncertainty
Location | 41.131°, -112.896° | 41.351°, -111.98° | 41.138°, -112.847° | 41.190°, -112.827° | 41.194°, -112.835°
Origin time | 12:06:00 | 12:08:02 | 12:06:14 | 12:06:24 | 12:06:23
, , | - | 20.6 km, 20.9 km, 83 sec | 10.6 km, 11.2 km, 38 sec | 11.2 km, 11.2 km, 36 sec | 15.0 km, 12.2 km, 43 sec
 | Ground Truth | BISL | A0 | 5 m/s uncertainty | 10 m/s uncertainty
Location | 41.131°, -112.896° | 41.351°, -111.98° | 41.138°, -112.847° | 41.190°, -112.827° | 41.194°, -112.835°
Origin time | 12:06:00 | 12:08:02 | 12:06:14 | 12:06:24 | 12:06:23
 | - | 20.6 km, 20.9 km, 83 sec | 10.6 km, 11.2 km, 38 sec | 11.2 km, 11.2 km, 36 sec | 15.0 km, 12.2 km, 43 sec

## Slide 21
Localization Confidence Trends
Modified detection sets and atmosphere ensembles have been constructed to investigate the impact of atmospheric uncertainty compared with detection quality
  Detection sets with f-stat values ranging from 5 to 200
  Atmosphere with values between 4 m/s and 20 m/s
Recently introduced stochprop Python tools enable construction of such ensembles
= 4, 12, and 20 m/s ensembles

## Slide 22
Localization Confidence Trends
General trends are as expected:
  Larger f-stat values decrease and resulting in smaller confidence ellipse area and increased precision
  Larger in the atmosphere ensemble increases the uncertainty ellipse area and decreases precision
Limited variations when is small and f-stat values are large, but dominates for larger values
= 4, 12, and 20 m/s ensembles

## Slide 23
Localization Confidence Trends
Relative variations are small for small f-stat values, but increase and become more strongly dependent on for f-stat > 20
Confidence is nearly constant for small and increase starting at values around values of 8 – 12 m/s

## Slide 24
Localization Confidence Trends
Relative variations are small for small f-stat values, but increase and become more strongly dependent on for f-stat > 20
Confidence is nearly constant for small and increase starting at values around values of 8 – 12 m/s
Poor detection quality dominates uncertainty
Atmospheric uncertainty dominates uncertainty

## Slide 25
Auxiliary parameters investigated for solving the Jacobian and computing geometric spreading can also be utilized in eigenray identification, weakly non-linear waveform evolution, and in localization likelihood construction.
The detection SNR can be used to quantify uncertainty in back projection launch angles
Application of the localization method to a synthetic multi-station event as well as an actual single-station multi-phase analysis show promising results
Sensitivity analysis related to the detection quality (f-stat) and atmospheric uncertainty (via ensemble analysis) shows complicated behavior in the uncertainty budget  continued sensitivity analysis is needed
Summary and Ongoing R&D

## Slide 26
Shameless Promotion
LANL SMEs authored an article in a recent issue of Acoustics Today detailing the history and current landscape of infrasound R&D for Nuclear Non-Proliferation.
https://acousticstoday.org/listening-for-a-boom-you-cant-hear/

## Slide 27
Questions?
https://github.com/LANL-Seismoacoustics