## Slide 1
Estimating Explosion Yields Using Fourier Neural Operators and Long-Range Infrasound Observations
Introduction Slide Title goes here [Font: Arial Bold/Size: 16]
P2.1-716
This poster presents a physics-informed Bayesian framework—powered by a fast Fourier Neural Operator surrogate—uses IMS infrasound to estimate explosive yield under realistic (gravity-wave) atmospheric variability for CTBT decision support.
On decade-scale Hukkakero events (IS37, 321 km), we achieve ~4 dB TL MAE and ~4 ms inference, recover yields in the 15–30 t range with tight 95% credible intervals via MLE+MCMC, enabling reliable yield estimations.
DISCLAIMER: This presentation has been generated for illustration purposes only.
Elodie Noëlé1,2, Christophe Millet1,3, Fanny Lehmann4
1CEA, DAM, DIF, F-91297, Arpajon, France, 2AMIAD, France, 3ENS Paris-Saclay, 91190 Gif-sur-Yvette, France
4ETH AI Center, ETH Zurich, Switzerland
Notes: 1

## Slide 2
❶ Surrogate Fourier Neural Operator for infrasound propagation
A one-dimensional, eight-layer FNO (~3 M parameters) learns the mapping from atmosphere to TL and achieves ≈4 dB MAE while evaluating a full TL field in ~4 ms (256 ranges r × 25 frequencies f).
❷Yield estimation with Maximum Likelihood Estimation and Markov Chain Monte-Carlo
Source parameters comes from numerical fits​, which parameterize Reed or Friedlander spectra. For a candidate yield, we use the surrogate to obtain TL-shaped near-source spectra (~ 2 km) and define a likelihood from the absolute spectral difference to the corresponding source model. We first locate the maximum via MLE, then quantify uncertainty with a simple Metropolis–Hastings sampler (2,000 warm-up, 10,000 draws), which produces stable, narrow posteriors around the expected tens-of-tons range.
Problem & Motivation
Estimating Explosion Yields Using Fourier Neural Operators and Long-Range Infrasound Observations
P2.1-716
Elodie Noëlé1,2, Christophe Millet1,3, Fanny Lehmann4
1CEA, DAM, DIF, F-91297, Arpajon, France, 2AMIAD, France, 3ENS Paris-Saclay, 4ETH AI Center, ETH Zurich, Switzerland
DISCLAIMER: This presentation has been generated for illustration purposes only.
Dataset
We aim to characterize explosive yield from IMS infrasound so that CTBT analysts can decide whether an event is consistent with non-nuclear activity or merits escalation. As a controlled case, we use the long-running Hukkakero chemical explosions in Finland—reliably recorded at IS37 (≈321 km)—whose yields W are in the 15–30 t range.
The main obstacle is atmospheric variability, especially gravity-wave–driven wind/temperature fluctuations in the stratosphere that refract sound ducts and alter effective celerity, making propagation both uncertain and expensive to simulate numerically due to statistical dispersion. Our approach combines a fast, physics-informed surrogate for propagation with a Bayesian inference scheme that turns station recordings into yield estimates with credible intervals. The scientific question is straightforward: can we reliably separate nuclear-scale from non-nuclear-scale yields under realistic atmospheric variability using Bayesian analysis of infrasound?
Methodology
We synthesize a training corpus of ~20,000 effective-celerity profiles a representing ten years of Hukkakero-like conditions, with and without gravity-wave perturbations. For each profile, a normal-mode solver (FLOWS) provides 1D transmission loss u across 25 frequencies between 0.06 and 1.5 Hz and ranges from 1 to 351 km.
Hukkakero #96 (19 Aug 2022). Gravity-wave perturbations drive strong dispersion in transmission-loss across selected frequencies, with gains up to ~20 dB; the bold black curve is the no-GW baseline.
Notes: 2

## Slide 3
Estimating Explosion Yields Using Fourier Neural Operators and Long-Range Infrasound Observations
P2.1-716
Conclusion & Future Directions
Results for Hukkakero event of 08/19/22
References
Under realistic atmospheric variability, a physics-informed ML surrogate coupled with Bayesian inference reliably estimates yields in the 15–30 t regime from IMS infrasound, providing transparent uncertainty and supporting characterization of non-nuclear and nuclear-scale events for CTBT decision-making. We will extend to 2D waveform propagation and seismo-acoustic coupling, and harden a real-time pipeline with adaptive frequency selection for operational deployment.
❷ MLE + MCMC
❶ Inference with surrogate FNO for 132 profiles
û = FNO(a)
Dellaportas, P., Roberts, G.O. (2003). An Introduction to MCMC. In Spatial Statistics & Computational Methods, LNS 173, Springer. Blom, P.S., Dannemann, F.K., Marcillo, O.E. (2018). Bayesian characterization of explosive sources using infrasonic signals. GJI 215(1):240–251. doi:10.1093/gji/ggy258.
Bertin, M., Millet, C., Bouche, D. (2014). A low-order reduced model for the long-range propagation of infrasound in the atmosphere. JASA 136(1):37–52. doi:10.1121/1.4883388.
Lehmann, F., Gatti, F., Bertin, M., Clouteau, D. (2023). Fourier Neural Operator surrogate model to predict 3D seismic waves propagation. arXiv:2304.10242.
Li, Z., Kovachki, N., Azizzadenesheli, K., et al. (2021). Fourier Neural Operator for Parametric PDEs. ICLR; arXiv:2010.08895.
Likelihood for each W
TL PDF û for 131 w/ GW + 1 w/o GW profiles of event 96
Single-frequency TL density and yield likelihood (W = 1–100 t). The Friedlander source model produces multi-modal structure: a dominant peak near ~18 t and a surface-burst alias close to ~36 t (≈2×), reflecting amplitude–duration ambiguity.
û
a
Elodie Noëlé1,2, Christophe Millet1,3, Fanny Lehmann4
1CEA, DAM, DIF, F-91297, Arpajon, France, 2AMIAD, France, 3ENS Paris-Saclay, 4ETH AI Center, ETH Zurich, Switzerland
Notes: 3