## Slide 1
DATA FUSION BETWEEN INFRASOUND
AND ELECTROMAGNETIC PULSE (EMP)
Maayan Kahlon1,2, Azi Lipshtat 1, Colin Price 3, Anthony J. Weiss 2
1 Israel NDC, Soreq Nuclear Research Center, Yavne, Israel
2 Dept. of Electrical Engineering, Tel Aviv University, Israel
3 Dept. of Environment and Earth Sciences, Tel Aviv University, Israel
Presentation number O2.1-061

## Slide 2
Goal
To examine the possibility of improving the analysis process of atmospheric infrasound events under the Comprehensive Nuclear-Test-Ban Treaty (CTBT)
Data Fusion Between Infrasound
and Electromagnetic Pulse (EMP)
Maayan Kahlon, Azi Lipshtat, Colin Price, Anthony J. Weiss

## Slide 3
Nuclear events emit both infrasound and EM signals
An infrasound signal which is not accompanied by an EM signal is not a nuclear event
An Infrasound event which is accompanied by EMPs requires further analysis (unless it can be shown that the EMPs are lightning)
Rational

## Slide 4
Most common EMPs are generated by lightning
There are 45 lightning per second occurring on earth
Lightning EMP may coincide with infrasound
The challenge

## Slide 6
Monitoring systems

## Slide 7
Infrasound event
EM recording
Coincide in time and direction?
All EMPs are lightning?
Detect EMP events
Not nuclear
Not nuclear
Analysis required
No
No
Yes
Yes
Methodology

## Slide 8
Infrasound Events
Infrasound SEL3 events from 36 non-consecutive days
580 events overall

## Slide 9
Single station – one component of electric field and two perpendicular components of magnetic field
Measurements from the same 36 days as the infrasound data
About 5 million events detected (300 Tb of data)
EM Measurements

## Slide 10
All infrasound events coincided with EMP events in time
49% that coincided in both time and azimuth
These events require further analysis
Infrasound – EMP Time and Azimuth Fusion

## Slide 11
Labeled Data
Simulations of Nuclear explosions
Lightning=

## Slide 12
Features Extraction

## Slide 13
Unsupervised linear method for dimension reduction
Preserving as much of the data's variation as possible
Started with D=19 dimensional features space
Dimension reduced to d=10 preserved 95% of the variance
Principal Component Analysis (PCA)

## Slide 14
k Nearest Neighbors algorithm with k=5
10-Fold cross validation for train – test split
Repeat 10 times with different groups of lightning
Classification

## Slide 15
Machine Learning – Model Validation

## Slide 16
After all EM events which coincided with IS events were projected to the PCA space and were classified, the results show:
All EMPs were classified as lightning
No infrasound event required further analysis
Results

## Slide 17
STEP | INPUT | TIME MATCH | TIME & AZIMUZH MATCH | CLASSIFICATION
# Infrasound events | 580 | 580 | 284 | 0
# EMP events | 5000000 | 48318 | 1682 | All lightning
Results

## Slide 18
Time and azimuth fusion between infrasound and EMP is not sufficient to eliminate all non-nuclear infrasound events
Lightning EMP and Nuclear EMP can be discriminated using their properties
Infrasound analysis can be improved when fusing with EM data
Conclusions

## Slide 19
  Real time data fusion in the single station level
  A more accurate detection in time and location can be obtained by multi-station system
  Cooperation with existing lightning detection networks
  Train the ML model on a larger data set
Future Work